## Slide 1: Monitoring and Control Over the Web
Martin Svestka Industrial Automation
Product Support Engineer Wed Aug 16
10:15-11:30 a.m., 1:45-3:00 p.m.
Cedar (8C)
Notes: The web is quickly becoming a tool to do almost everything. Learn how you can leverage the power of the web to monitor and control applications ranging from laboratory environments to industrial applications. This session covers tools like Lookout web client and LabVIEW internet toolkit. Lookout web technologies that can transform your application to a web-based one.
Equipment you need for this presentation:
Hardware:
A computer running a Windows operating system
FieldPoint Demo box (FP-1600, AO, IA, DO, Crossover Ethernet cable, PS-2 power supply)
Software:
LabVIEW 6.0 with Internet Toolkit 5.0
FieldPoint 2.0 or higher (ftp://ftp.ni.com/support/fieldpoint/Server)
Lookout Development server 4.0.1 or higher, Lookout Client License
Internet Explorer 4 or higher
Apache Web Server v1.3 (http://www.apache.org/httpd.html go to Download! Link)

## Slide 2: Agenda
Distributed execution
Present and control
Technologies overview
Lookout
LabVIEW web server
LabVIEW internet toolkit
Notes: Distributed execution
Present and control
Technologies overview
Lookout
LabVIEW web server
LabVIEW internet toolkit

## Slide 3: Acquire, Analyze, and Present
Acquire
Analyze
Present
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
As we look at the history of acquiring data, scientists and engineers took some of the first measurements using electrical devices, such as analog meters, that were crude by today’s standards. Over time, these devices evolved into increasingly sophisticated and complex stand-alone instruments, such as spectrum analyzers and vector network analyzers. While delivering a marked increase in measurement capability and flexibility, these instruments had and still have a number of limitations; they generally do not permit the user to modify the set of functions or operations they can perform. This is because the data acquisition, analysis, and presentation properties of the instrument are determined by the vendor and are not subject to alteration. The whole concept of virtual instrumentation is to create measurement systems by combining measurement hardware and software components with mainstream computer technologies, such as desktop PCs or workstations. By incorporating industry-standard computers into your system architecture, you effectively capture superior processing power, performance, and data storage in your measurement system.
Many measurement systems today only contain a single computer. What would happen if we were to expand such a system to include more than one computer or even span an entire network? By doing this, you can capture all of the advantages networks provide for your measurement application.

## Slide 4: Distributed execution
Acquire
Analyze
Present
Control
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
Distributed execution allows you to execute various tasks in your measurement and automation system across several different computers so that no one machine becomes stressed under a heavy load of the required operations. Additionally, you can coordinate measurement operations across many computers into a single system. You can acquire and reduce data at the computer taking the measurement. Reducing your data before sending it helps reduce network congestion.
You can use distributed execution to control a system remotely. You can split execution so that the measurement system can reside on a remote machine and the controlling portion resides on a computer in a more comfortable location.
Distributing execution provides some definite advantages. You can selectively choose which portions of your cumulative measurement tasks run on which machines, often in parallel, resulting in improved system performance. Moreover, because you can distribute your application in such a way that no single computer becomes a bottleneck in your measurement system, these systems will not be as taxed. Distributing execution means you can protect your computer capital investment.
A typical measurement solution consists of an acquisition element, an analysis component, and some type of presentation capability. With distributed execution, you can break up these tasks and run them on different computers. No longer is it acquire, analyze, and present - it’s acquire anywhere, analyze anywhere, and present anywhere.

## Slide 5: Technologies for publishing

## Slide 6: Lookout client/server
Lookout clients
Lookout server
FieldPoint
Notes: Lookout servers are computers that are connected to your field hardware by cables and wires. Typically server processes that run in the server computer has drivers that connect to the hardware. Client computers that has the nice HMI/operator interfaces connect to the server computers.
A Lookout client process can be run on the same computer as a Lookout server, or it can be moved and run on any computer on the same network as a Lookout server. Client processes cannot not connect directly to your field hardware. Client processes interact with hardware through a server computer.

## Slide 7: Lookout web client/server
Lookout clients
Lookout server
Web server
Export
FieldPoint
Notes: Besides the standard Lookout client that requires an explicit installation of the Lookout Run-time to load and run any client process file you can use a web browser to load and run your process files. No additional installation is required for this configuration and no additional changes in the client process are required. All you do is export the client process to a directory. This step will create a set of files including an HTML page. This page is then loaded by a web browser on a client machine.
Web server and Lookout process server are two independent servers that can run on totally different machines.

## Slide 8: Lookout web client
FieldPoint reads/writes physical I/O
Lookout server communicates with FieldPoint
Lookout web client presents results
Notes: The following demonstration uses FieldPoint Ethernet module as a distributed I/O. Lookout server then communicates with the FieldPoint module. The server does not have any panel to present results. The only purpose of the server is to take care about I/O communication. We will have Lookout web client to present data.
You can create an HTML file to display a Lookout client that can then be accessed through a web browser and downloaded to a remote computer.
Lookout accomplishes this by creating a simple HTML page and inserting an ActiveX control on the page that runs your client process. When you create your HTML page, Lookout also creates an entire support package for that page, including a client version of Lookout and other support files so that users without Lookout installed on their computers can run the ActiveX control.

## Slide 9: Lookout demo – web server
Download Apache web server
  http://www.apache.org/httpd
C:\Program Files\Apache Group\Apache\htdocs is mapped to http://<web_server>/
Notes: The Lookout web client allows you to access a Lookout process from any networked machine via a web browser. This document describes the steps you should take to create sample client and server processes and run the client process over the Web using Internet Explorer.
Make sure you have AWS 1.3 (Apache Web Server) installed your on server machine. If you don't have AWS, then you can go to:
http://www.apache.org/httpd
for a free download. The AWS installer will place its files in a default directory called C:\Program Files\Apache Group\Apache\htdocs. This directory is mapped to http://<web_server>/ and this is the place where we will to install our lookout process file. On the picture the directory contains Process1.htm file exported by Lookout and two directories with all necessary support file. If you want to launch the client on in a web browser you need to type the web server name and client process file name with htm extension:
http://<web_server>/Process1.htm

## Slide 10: Lookout demo – export files
Generate client.htm and support files
  Create a process
  Set export directory and URL
  Launch export
  Close client process, load server process
  Launch web server
Notes: Open the client.l4p file and go to File >> Web Server Export Options >> Export Directory and enter the path where all your AWS files are located. In this example enter C:\Program Files\Apache Group\Apache\htdocs.
Go to Server URL and enter http://<web_server>/ and press OK.
Go to File >> Export Web Server Files >> Select Process to Export and select OK. A dialog box will appear with the message "Web Server Export in Progress."
Close the client process. This is necessary if you are about to launch the web client on this computer, since you cannot have two processes with the same name running at the same time. Open the server process (server.l4p) if it is not already open.
Start and verify the web server.
On Windows NT: To start Apache as a service, you first need to install it as a service. To install the default Apache service named "Apache", run the "Install Apache as Service (NT only)" option from the Start menu. Open the Services window (in the Control Panel), select Apache and click on Start.
On Windows 9x: Go to Start >> Programs >> Apache Web Server >> Start Apache. Later Select Stop Apache to stop the web server.
Verify that the web server is functional. Launch the Internet Explorer and type: http://localhost. You should receive a welcome page.

## Slide 11: Lookout demo – launch client
Start Internet Explorer
Make sure security is set to Low
Type:
  http://<web_server>/client.htm
Notes: Launch Internet Explorer on the local or any other networked computer. Select Tools (View in the IE4) >> Internet Options >> Security and make sure that security is set to low for Local Intranet. This is necessary to run active content. If you want to access this page over the Internet, repeat this step for Internet settings.
Type http://<web_server>/client.htm in the address box.
Internet Explorer will bring up a dialog box stating "This page provides unsafe ActiveX controls." There is no need to be concerned with this message - just press OK. You will see another dialog box stating "Lookout Web Control will now download files." Click OK, and you should be finished.
If nothing appears try to relaunch the web browser.
NOTE: It is very important to have a Lookout Client License on your server machine. The Client License is National Instruments part number 778102-01.

## Slide 12: LabVIEW
LabVIEW built-in web server
LabVIEW internet toolkit

## Slide 13: LabVIEW built-in web server
You don’t need any additional toolkit
View or monitor your virtual instruments
Set security
  Based on IP address
  Based on VI name
Notes: LabVIEW is shipped with a built-in web server. The server can be enabled from Tools >> Options >> Web Server: Configuration. Ones the server is enabled you can start a web browser and type: http://<server_name>. If you are running browser on the same machine as LabVIEW computer name can be specified as localhost (type http://localhost).
LabVIEW web server security is based on the client address and/or VI names. You can list client IP addresses that are allowed/denied to connect to the server and you can specify a list of VIs that can be accessed/denied.

## Slide 14: LabVIEW – view and monitor VIs
http://<server>/.snap?Webtest.vi
http://<server>/.monitor?Webtest.vi
Notes: Once you have connected to the server, you can actually have the server send you just one picture of the front panel of a VI (that is currently open) by using the .snap? command, or you can have it send you a collection of pictures in memory by using the .monitor? Command. For example:
http://localhost/.snap?Webtest.vi
or
http://localhost/.monitor?Webtest.vi
Notice that no programming is required to accomplish this task.

## Slide 15: LabVIEW internet toolkit
View or monitor your virtual instruments
Incorporate security based on users
Send e-mail
Send files or raw data (FTP client)
Build Common Gateway Interface (CGI)
Notes: Internet-Enabled Applications
With a toolkit, you can build your own HTTP server using LabVIEW to make your virtual instrument front panels viewable from any web browser. Your panels will automatically update as animated virtual instruments across the web using client-pull or server-push update methods. You can control access to your virtual instruments based on user name and password, or based on the user's IP address.
E-Mail and FTP-Enabled Virtual Instruments
You can automatically send e-mail based on a set of conditions, send files or raw data to an FTP server from your applications. These are key capabilities for any remote field monitoring and control applications that must pass data to a centralized reservoir or keep operators up to date on the system status.
Build Common Gateway Interface (CGI) Programs in G
CGIs are used to make decisions dynamically based on user input on a web page. CGIs have a standard API for receiving a response from a remote user and taking action, such as checking an end-user name and password against a valid user list, returning a different HTML page to user, making a computation and returning the results, or dynamically building an HTML page based on the data passed.

## Slide 16: LabVIEW – send e-mail
Send a notification when alarm occurs
Send raw data or files
Refer to shipped examples
Notes: You can automatically send e-mail based on a set of conditions. These are key capabilities for any remote field monitoring and control applications that must pass data to a centralized reservoir or keep operators up to date on the system status.
For an example how to use E-mail VIs, go to Tools >> Internet Toolkit >> Internet Toolkit Examples.

## Slide 17: LabVIEW – CGI
Launch VI remotely from your browser
Pass parameters to your VI
Notes: The LabVIEW CGIs enable the programmatic launching, viewing, interaction with VIs. You can even pass parameters between your web browser and LabVIEW using the CGIs (with significant tweaking). The examples page (the default page that ships with the toolkit) will demonstrate that and more. It will even show how to password protect your application.
The way that the Internet toolkit fits in with the rest of the NI vision for control/analysis, is that it specifically enables browser to LabVIEW communication. Unlike a number of other options which are really LabVIEW to LabVIEW or VB to LabVIEW.
So, to have a higher level of control of your applications, our recommendation is the internet toolkit.

## Slide 18: LabVIEW – CGI example
<HTML>
<FORM METHOD=post ACTION="cgi-bin/temp.vi">
Notes: This example demonstrates CGI functionality.
First of all, make sure LabVIEW Internet toolkit server is running and the built-in server is stopped. Both of them are listening on the same port and they would be in a conflict. Uncheck the Enable Web Server in the Tools >> Options… >> Web Server: Configuration to stop built-in server. Select the Tools >> Internet Toolkit >> Start HTTP Server… to start the Internet toolkit server.
Make sure you have temp.vi in the <LabVIEW>\internet\home\cgi-bin directory.
Open Internet Explorer and type: http://localhost/temp.htm
The page similar to the one on the slide should be displayed. Enter some value in the two edit boxes and press Submit Query button. This will send ACTION string (ACTION="cgi-bin/temp.vi) to LabVIEW Internet toolkit. The string tells LabVIEW to run the temp.vi from the cgi-bin subdirectory (the VI does not have to be running). In addition, it will pass some parameters to this VI, including the entries from the edit boxes. Their IDs are Temperature and Location. The VI then calls CGI Read Request.vi to read these parameters and their values and displays the values on the panel.
As a reply to the page submit the VI sends back a “Temperature adjusted” string to the browser that gets displayed. This is going to be done by the CGI Write Reply.vi. Make sure the every session is always released by CGI Release.vi.

## Slide 19: Measurement Studio
LabWindows/CVI Internet toolkit
Component Works

## Slide 20: LabWindows/CVI Internet toolkit
Monitor/control your panels (Web server)
Incorporate security based on user/host
Send e-mail
Send files or raw data (FTP client)
Notes: You can use the LabWindows/CVI Internet Developers Toolkit to display your LabWindows/CVI user interface panels on the Internet. Users of Web browsers can click on these panels to interact with your LabWindows/CVI applications. The toolkit provides a mechanism to automatically convert a user interface panel into an image that any client using a Web browser can access.
Users viewing a user interface panel in their Web browsers can actually click on controls. The coordinates of these mouse-clicks are then passed over the Internet directly to the LabWindows/CVI program running on the server, where they are processed as if a local user were operating the panel. This capability provides a limited level of remote control of your user interface panels over the Internet.
The LabWindows/CVI Internet Developers Toolkit also includes functions for adding e-mail and FTP file transfer functionality to your LabWindows/CVI programs. Using the client-side e-mail and FTP file transfer capabilities, you can automatically send files to an FTP server from your application or automatically send e-mail when alarm conditions occur. Clients can also download updated configuration or data files from an FTP server.

## Slide 21: LabWindows/CVI - control panels
Register your program as a web server
Export a periodically updated image of panels
Enable web browser input on exported panels
Demonstration – autoupdt.prj
Notes: To use any of the features of the LabWindows/CVI Web Server, you must call INET_StartWebServer. This function creates a new instance of the LabWindows/CVI Web Server. For example:
webHnd = INET_StartWebServer (80, 10, "", "");
Export a periodically updated image of a panel when you want to give users a live view of an ongoing process. Call INET_RegisterPanelAutoUpdate to do it. For example:
INET_RegisterPanelAutoUpdate (webHnd, panelHnd, INET_UPDATE_SERVERPUSH, "exper.jpg", 0, 15.0, 0);
To enable input on a panel through a Web browser, you must export an image of the panel and then register the panel for input. When a user of a Web browser left-clicks on the panel image, the client computer sends the coordinates of the click to the Web server. The LabWindows/CVI User Interface Library then processes a mouse click as if it had occurred on the server machine at those coordinates. For example:
INET_RegisterPanelWebInput (webHnd, panelHnd, “exper.map",0);

## Slide 22: Component Works weather station
Acquisition
LabVIEW
Remote SCXI
Distribution
LabVIEW
DataSocket server outside firewall
Web Clients
DataSocket Client
Web browser weather monitors
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
Live weather stations is an excellent example of distributed execution. The weather conditions in Austin, Texas at National Instruments headquarters are published on the Internet. Log to http://ni.com/datasocket/ds_websol.htm site to view a real-time display of the weather conditions.
To collect the weather information, a remote SCXI chassis with various signal conditioning modules interface to the various weather instruments for measuring the current weather conditions. This SCXI chassis and signal conditioning modules are controlled using LabVIEW.
Not only is LabVIEW used to actually acquire the weather measurements, it also distributes the data. It does this by posting data updates to the DataSocket Server which is located outside our Internet firewall. This isolates the publishing of the acquisition data from National Instruments internal network. Thus anyone can log can run our weather applications and get weather updates from Austin. The DataSocket server publishes all the data from the weather station to any Web clients that connect to the weather monitoring applications. This is a streaming data publishing technology and all data collected by the weather system is sent to the client Web browser as quickly as its collected.

## Slide 23: Summary
Distribute your system execution
Use the Internet/Intranet to publish & control
National Instruments development tools support Internet technologies
Notes: The Internet/Intranet makes it easier to distribute execution. You can selectively choose which portions of your cumulative measurement tasks run on which machines, often in parallel, resulting in improved system performance. Moreover, because you can distribute your application in such a way that no single computer becomes a bottleneck in your measurement system, these systems will not be as taxed.
You can use the Internet to make your application distributed. The Internet is not only limited to monitor remote process, but you can also use it to control the process. All National Instruments product are Internet ready and you can use them to build your own distributed system.

## Slide 24: Configuring Lookout demo (1)
FieldPoint
  HW configuration
  SW configuration
Lookout
  Modify server process
  Modify client process
Web server
  Install Apache web server
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
Configuring Lookout demo
Before demonstration
The Lookout demo will connect to the FieldPoint demo box. Follow these instructions to set up the demonstration before it will be started. All support files for this demonstration should be saved in a Demo directory on the computer desktop to minimize necessary changes. The files includes: FP Conf.iak, client.* and server.* files.
Reading TCP/IP configuration
Before starting the configuration make sure you know your computer IP address and Subnet mask. To find out run winigcfg from Start >> Run on Windows 9x, or ipconfig from MS-DOS prompt on Windows NT/2000. We will you this address to derive the FP-1600 IP address. We can do it this way because we know that we are not going to be connected to a network, so we cannot get an IP address conflict.
FieldPoint HW configuration
Reset the network module (refer to FP-1600 User manual, Appendix A for more details; http://www.ni.com/pdf/manuals/322394a.pdf)
Connect the demo box to your computer over the Ethernet crossover cable

## Slide 25: Configuring Lookout demo (2)
FieldPoint
  HW configuration
  SW configuration
Lookout
  Modify server process
  Modify client process
Web server
  Install Apache web server
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
FieldPoint SW configuration
Launch FieldPoint Explorer and open the FP Conf.iak file
Right click on the FP Res entry and select Edit this comm resource…
Click Browse… and you should get Unconfigured entry in a new window
Highlight this entry and click Device Properties
Configure IP addresses as follows:
  IP address: IP address of your computer that differs in the last number (e.g. if you computer name is 130.164.58.5, enter 130.164.58.6). Note: If you computer is not on network you don’t have to worry about the a possible conflict with another computer.
  Subnet mask: enter the subnet mask you figured in the step 1
  Gateway IP: 0.0.0.0 (we are not on any network)
  DNS server IP: 0.0.0.0
  Time server IP: IP address of your computer
Click OK twice and then Find Devices
The module names should be FP-1600 @0 and FP-AI-100 @1, FP-AO-200 @2, FP-DO-401 @3
Verify that module is working – select I/O >> Start monitoring
Save you changes and close FieldPoint explorer

## Slide 26: Configuring Lookout demo (3)
FieldPoint
  HW configuration
  SW configuration
Lookout
  Modify server process
  Modify client process
Web server
  Install Apache web server
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
Lookout
Open the server.l4p. Select Object >> Modify… >> FieldPoint1.
Change the IP address to the one that you have assigned the FieldPoint.
Check the Import alias information, click Browse and reload the FP Conf.iak file
Click OK to close the FieldPoint1 window
Save changes
Open the client.l4p. Select Object >> Object Explorer…
Right click on the [Server] symbolic link in the Object Browser and select Properties…
Change the computer name (//martin) to your computer name
Click OK to close the window. Change the pot value in the demo box…. Note: If you don’t see traces check the Y-axis range of the Trend object

## Slide 27: Configuring Lookout demo (4)
FieldPoint
  HW configuration
  SW configuration
Lookout
  Modify server process
  Modify client process
Web server
  Install Apache web server
Notes: WS1C-<number>
Remote Monitoring and Control Over the Web
<header>
<date/time>
Install web server
You should have already downloaded the Apache Web Server on your computer (apache_1_3_12_win32.exe)
Run the download, keep default pathname for the installation (C:\Program Files\Apache Group\Apache\htdocs)
Start the web server
  On Windows NT: To start Apache as a service, you first need to install it as a service. To install the default Apache service named "Apache", run the "Install Apache as Service (NT only)" option from the Start menu. Once this is done you can start the "Apache" service by opening the Services window (in the Control Panel), selecting Apache, then clicking on Start. Apache will now be running in the background. You can later stop Apache by clicking on Stop.
  On Windows 9x: Go to Start >> Programs >> Apache Web Server >> Start Apache. Later Select Stop Apache to stop the web server.
  Verify that the web server is functional. Launch the Internet Explorer and type: http://localhost. You should receive a welcome page.

## Slide 28: Configuring LabVIEW CGI demo
Internet toolkit
  Install toolkit
Demo files
  Copy temp.vi to <LabVIEW>\internet\home\cgi-bin
  Copy temp.htm to <LabVIEW>\internet\home
Notes: Configuring LabVIEW CGI demo
Before demonstration
Temp.htm page has a button that will command the Internet toolkit to launch temp.vi. Before this demo can run make sure that Internet toolkit is installed on the computer and temp.vi is copied in the <LabVIEW>\internet\home\cgi-bin subdirectory and temp.htm in the <LabVIEW>\internet\home subdirectory.