## Slide 1: Building User Interfaces with LabVIEW™
Steve Symons
Senior Software Engineer
Wed Aug 16
12:00-1:15 p.m., 3:30-4:45 p.m.
Cedar (8c)
Notes: Learn to develop professional user interfaces quickly and easily in G. The discussion includes layout, colors, decorations, using the control editor, event-driven programming, and more.

## Slide 2: Agenda
Introductory topics
  Colors
  Spacing and alignment
  Importing graphics/making pictures
Examples
  Control editor
  Event-driven programming – state machine
  Resize panel
  Tab control – dialog box
  Active X controls
Conclusion and questions

## Slide 3: Complementary Colors
Colors are not ugly, combinations are!
Color scheme implies mood
Choose a scheme and stick with it
Do not use color inappropriately
Gray is safe, but a little boring
Notes: <number>
<footer>
Colors are not ugly in isolation. Combinations of colors can compliment or clash. As a rule, avoid clashing colors. The schemes on the slide are primary, skin-tone, sand, and pastel. A given color may belong to many schemes. Stay within one scheme to avoid clashing.
Primary colors denote that something is simple or childlike. Some schemes are warm and earthy while others are cold and harsh. Notice how these color descriptions are very different from the red-green-blue (RGB) value of an individual color. They really apply to color schemes.
Fire-engine-red looks good on fire engines and sports cars. It is a poor choice for the paper color of a resume. Virtual instruments (VIs) that are all gray may be boring, but as long as they have enough contrast, they are very easy and quite professional.
Easy technique:
  Start with a gray scheme
  Add highlight colors sparingly to match logo or existing colors
  Use color only for plots, errors, and maybe an abort button
  There are better and easier grouping techniques than color
Good places to learn about color are maps, magazines, and nature – anywhere except the computer screen.

## Slide 4: Spacing and Alignment
Use space to separate objects and also to group them
Justification works better than center alignment
Use decorations to group objects
Jonathon Doe
Guru/Geek
555-1212
Tech Central
Austin, TX
78787
Guru/Geek
Tech Central
Austin, TX
78787
Call Me!
555-1212
Jonathon Doe
Notes: <number>
<footer>
White space and alignment are probably the most important techniques for grouping and separation. The more items that your eye can find on a line, the more cohesive and clean the organization seems. When items are on a line, the eye follows the line from left to right or top to bottom. This is related to the script direction. Although some cultures might see items right to left, almost all follow top to bottom.
Centered items are better than random, but much less orderly than either left or right. Note that a band of white space acts as a very strong means of alignment. Centered items typically have ragged edges and the order isn’t as easily noticed.
Cosmetic items or decorations are useful for grouping and reinforcing alignment. Also, there are certain cosmetic groupings to avoid, particularly boxes within boxes.

## Slide 5: Using Pictures and Images
Metafiles(PC)/PICTS(MAC)
ISA symbol toolkit
Displaying BMPs
Picture control
Notes: You can use metafiles on the PC and PICT files on the Macintosh in place of bitmaps.
These file formats support non-rectangular pictures, transparency, and are scalable. Try importing \pictures\ant.wfm and \pictures\ant.bmp files into LabVIEW™ to see how they differ. Also look at \pictures\button.vi for an example of a button with a transparent center.
You can use the pict ring to store bitmaps which enables you to dynamically switch between them and create animation effects on your front panel.
See \pictures\engine.vi (on the NIWeek 99 CD) for an animation example.
You can also use the intensity graph and picture control as a method for dynamically displaying bitmaps on your front panels.
See \pictures\BMP Read.vi (on the NIWeek 2000 CD) for an example.

## Slide 6: Example 1 – Control Editor
Not used often enough
Very powerful tool
Example 1 – three-position toggle switch
Notes: The Control Editor is a great tool. Its potential is often underestimated. We have already used its capabilities several times during this presentation.
See Exercise 1 in the handout for directions on how to build a three-position toggle switch.

## Slide 7: Example 2 – Event-Driven User Interfaces
Responds in a reasonable time
Does not use all the CPU time polling
Notes: Event-driven user interfaces provide structure and efficiency to your applications. A couple of methods have been discussed in the LabVIEW Technical Resource (LTR), but the main ideas are as follows:
1. The outermost structure of your application is a continuous While loop that looks for user input or change.
2. All user inputs or changes are reduced to Boolean events, which are handled in a consistent manner.
3. A state machine handles events.
In Exercise 2, you will modify a VI that uses two sub-VIs for handling events in an event queue:
1. Add Panel and Menu Events.vi: Accepts events from a boolean array and from a menu and combines them and places them in a string array queue. If no event is detected, the VI waits a short duration to free up computer resources for other applications.
2. Get Next Event.vi takes the next event off the queue and uses it to select from a series of event cases.

## Slide 8: Example 3 – Window Resizing
Modify a VI to take advantage of window size
Notes: VirtualBench™ implements this by checking with the server or VI control to detect window sizing changes. When a size change is detected, it calculates new locations and sizes for the controls and uses attribute nodes to place the controls and indicators in their new locations with their new sizes.
First, determine what control(s) you wish to grow when the window changes size. Then, determine which control(s) need to move out of the way and stick to the edge. As with other attribute node intensive code, any controls placed into clusters simplifies the number of attributes needed.

## Slide 9: Example 4 – Tab Controls
Examine a VI which uses a tab control to implement an interactive dialog box
Notes: Open “Tab Control Example.vi”
Notes:
The front panel is configured to be resizable around the graph.
Dialog controls and dialog box front panel window settings reflect system colors.
Items can be controls or indicators.
Indicators on other tabs are not drawn so there is little performance penalty.

## Slide 10: Example 5 – ActiveX controls
Create a VI to read the date from a calendar ActiveX control
Notes: Advantages – many ActiveX controls can are available on the Web and sold as packages.
Disadvantages:
1. Not as easy to use as built-in LabVIEW controls
2. Only available for Windows 9x/NT OS
3. LabVIEW applications must include and register .OCX files
In exercise 4 you build a VI that reads the date selected from a calendar activeX control and displays the formatted date in a string indicator. Please refer to your handout for the exercise.

## Slide 11: Control Features in LabVIEW 6i
3D controls and line decorations
Multiple scales on graphs and charts
Multicolumn listbox
Color ramp for rotary controls
Digital graph, logic analyzer display
Notes: <number>
<footer>
One of the most powerful UI feature in LabVIEW 6i is a diagram feature. Attribute nodes can now be located in subVIs where they are shared across multiple panels and clean up top-level diagrams. Use them carefully or you will introduce race conditions that are difficult to debug. In the past you knew an attribute was being changed somewhere on the diagram and you could even Find each and every attribute. Now the Control reference can be passed to any number of subVIs running in parallel and making changes to the UI without synchronization. It is a great power user feature, but beware of the debugging headaches.
3D controls may be the most noticeable feature in LabVIEW 6i. Some of the controls look nice, but they are not a quick fix for poorly designed panels. Use the same rules for association and coloring, and your panels should look nice.
Graphs and charts now have good support for multiple scales, scale name labels, and programmatic control over more attributes.
There is a new control that works well for lists of multicolumn data, like file system lists that include the data or size.
You can popup on a meter or gauge and view the rotary color ramp. It allows you to associate a color with arbitrary markers on the scale so that you can have color bands and color ranges beneath the needle.
Digital graph and logic analyzer display. The waveform graph now knows how to plot lines and groups of lines much like a logic analyzer. Use the mask data element to specify which bits are placed into which plot and in which order.
You can now give your buttons or other controls a tip strip in addition to the information that shows in the help window.
Once you have associated controls using space, borders, or white space, group them to maintain the association and manipulate them as a group. You can also lock decorations and other background objects so that they stay in the background. They will not be accidentally deleted or moved, and you can also popup to drop new controls as if they were a part of the background.
There are many other control and panel attributes/properties that allow better programmatic control over how the UI works. The value of the control can be read/written to from the property node, making it possible to update many properties and the data all at once with less flicker. There is also a panel attribute for turning off updates while many attributes or data values are updated, then restore the value to update the panel.

## Slide 12: Editor Features in LabVIEW 6i
Control references
  A SubVI can make attribute changes
  Use it to share code and clean up diagrams
Tip strips on controls
Group and lock
New control and panel attributes
Notes: <number>
<footer>

## Slide 13: Resources
LabVIEW Technical Resource
Info-LabVIEW
National Instruments Web site or FTP site ni.com ftp.ni.com
Notes: Many resources exist for solving user interface challenges.
The LabVIEW Technical Resource is a quarterly periodical packed full of great LabVIEW programming information. For more information contact:
LTR Publishing
6060 N Central Expressway, Suite 502
Dallas, TX 75206
Tel: (214) 706-0587, Fax: (214) 706-0506
e-mail: ltrpub@aol.com
Try info-labview if you want to ask your LabVIEW peers for user interface or general LabVIEW coding suggestions. The info-labview archive is a great place to look for code that other LabVIEW/BridgeVIEW™ users were kind enough to make public. Info-labview has been in operation since February 14, 1991.
You can get to info-labview by pointing your browser to http://k-whiner.pica.army.mil/info-labview/info-labview.html
You can also send e-mail to info-labview-request@pica.army.mil and ask to be added to the mailing list.
Try National Instruments Web site, ni.com, or our anonymous FTP site, ftp.ni.com, as well.