## Slide 1: Synchronizing DAQ with In-Vehicle Communications
Zaki Chasmawala
CAN Software Engineer
Thurs Aug 17
10:15-11:30 a.m., 1:45-3:00 p.m.
Cedar (8C)

## Slide 2: Agenda
Automotive test systems
CAN – introduction, benefits, markets
CAN basics
Brief overview of NI-CAN™
Typical automotive test applications
Synchronization capabilities in NI-CAN 1.4
Demo with NI-DAQ™
Demo with NI-IMAQ™
Notes: The purpose of this presentation is to:
1. Introduce NI-CAN as a platform for CAN based automotive test system.
2. Offer a hardware based synchronization solution between the traditional DAQ based test system and the CAN based test system

## Slide 3: Current Automotive Test Systems
High speed DAQ
Signal conditioning
Use of traditional sensors and transducers with point to point wiring
Move to CAN based test systems
Need the ability to synchronize DAQ-based systems with the newer CAN-based systems.
Notes: In the past few decades, the need for improvements in automotive technology has led to increased usage of electronic control systems for functions such as engine timing, anti-lock brake systems, and distributorless ignition.
With conventional wiring, data is exchanged in these systems using dedicated signal lines. As the complexity and number of devices has increased, usage of dedicated signal lines has become increasingly difficult and expensive.
With traditional sensors, transducers and wiring, current automotive test systems require a high speed DAQ board and a signal conditioning chassis (SCXI).
As automotive manufacturers are moving to in vehicle networks (whose advantages are discussed later), CAN based test systems are gaining importance along with the existence of DAQ based systems.
DAQ based tests systems remain in existence to verify the integrity of the newly developed CAN based systems.
Since data is acquired on the CAN and DAQ test systems , simultaneously, it has become essential to provide timing and triggering signal between the CAN and DAQ test system. This capability allows easy simultaneous charting, logging and correlation of the data acquired by each individual system.
As we will learn later, a hardware based synchronization solution is more effective and accurate than using a software based solution

## Slide 4: CAN (Controller Area Network)
Developed by Bosch in the mid 1980s for automotive in-vehicle communications. Also used in medical, agricultural, and machine control markets.
Backbone for several industrial protocols, such as DeviceNet, CANopen, SDS.
ISO 11898 (high speed CAN), ISO 11519 (low speed CAN).
Notes: To overcome the limitations of conventional automotive wiring, Bosch
developed the Controller Area Network (CAN) in the mid-1980s.
As CAN implementations increased in the automotive industry, CAN (high speed) was standardized internationally as ISO 11898, CAN (low speed - for car body electronics) was standardized as ISO 11519. CAN chips were created by major semiconductor manufacturers such as Intel, Motorola, and Phillips.
With these developments, many manufacturers of industrial automation
equipment began to consider CAN for usage in industrial applications.
By the mid-1990s, CAN was specified as the basis of many
industrial device networking protocols, including DeviceNet, CANOpen,
and Smart Distributed System (SDS).

## Slide 5: CAN Markets
In 1998
  Approximately 97 million CAN nodes sold
  80% in Europe -> 80% in Germany-> 80% in Automotive
  US Automotive moving to adopt
  Currently in Mercedes, BMW, Audi, Volkswagen, Saab, Renault, Fiat, Volvo, Cadillac
  Soon in Daimler/Chrysler, Ford, GM

## Slide 6: CAN – Automotive Market
Used in many systems
  Transmission
  Engine control – fuel injection, emissions, etc.
  ABS
  Lights
  Dashboards
  Power windows and locks
  Audio/video control
  Power steering

## Slide 7: Other CAN Markets
Public transportation
Maritime
Mobile/farm machinery
Embedded
Building controls
Military systems
Notes: Comparison of the requirements for automotive and industrial device
networks showed many similarities, including the transition away from
dedicated signal lines, low cost, resistance to harsh environments, and high
real-time capabilities.
Because of these similarities, CAN became widely used in industrial
applications such as textile machinery, packaging machines, and
production line equipment such as photoelectric sensors and motion.
With its growing popularity in automotive and industrial applications, CAN
has been increasingly used in a wide variety of diverse applications. Usage
in systems such as agricultural equipment, nautical machinery, medical
apparatus, semiconductor manufacturing equipment, and machine tools
testify to the incredible versatility of CAN.

## Slide 8: Benefits of CAN
Cost effective hardware
Very reliable, proven
Significantly fewer connections than traditional cable harnesses
  Reduced weight
  Lower manufacturing and operating cost
Low speed CAN (fault tolerant)
All the benefits of a digital network
  Real time capabilities

## Slide 9: Benefits of CAN – Wiring
Replaces existing cable harnesses with a multi-master 2-wire digital bus
  Maximum 1 Mbit/sec
    40 Meters at 1 Mbit/sec
    6 Km at 10 kbit/sec
  Maximum 2,032 nodes per bus (theoretical)
  Approximate 100 node practical due to transceiver
  3-10 nodes are used in practice
Notes: Using CAN, devices (controllers, sensors, and actuators) are connected on a
common serial bus. This network of devices can be thought of as a scaled
down, real-time, low cost version of networks used to connect personal
computers. Any device on a CAN network can communicate with any other
device using a common pair of wires.

## Slide 10: CAN – Basics (High Speed)
Up to 1 M bits/sec transmission rate
CAN arbitration ID (11 bit or 29 bit)
  Indicates message priority
CAN data (up to 8 data bytes in a frame)
If two devices transmit at the same time, lower priority object holds off until higher priority object is acknowledged
Remote transmission – method of requesting data (or action) from a device by transmitting a zero data byte frame
Notes: When a CAN device transmits data onto the network, an identifier that is unique throughout the network precedes the data. The identifier defines not only the content of the data, but also the priority. When a device transmits a message onto the CAN network, all other devices on the network receive that message. Each receiving device performs an acceptance test on the identifier to determine if the message is relevant to it.
When more than one CAN device transmits a message simultaneously, the identifier is used as a priority to determine which device gains access to the network. The lower the numerical value of the identifier, the higher its priority.
If an identifier collision is detected, the losing device(s) immediately cease transmission, and waits for the higher-priority message to complete before automatically retrying. Because the highest priority identifier continues its transmission without interruption, this scheme is referred to as non-destructive bitwise arbitration, and CAN’s identifier is often referred to as an arbitration ID. This ability to resolve collisions and continue with high-priority transmissions is one feature that makes CAN ideal for real-time applications.
A device transmits a remote frame to request transmission of a data frame for the given arbitration ID. The remote frame is used to request data from its source device, rather than waiting for the data source to transmit the data on its own.

## Slide 11: CAN Basics (Low Speed)
Up to 125K bits/sec transmission rate
Used in “comfort” applications
Special cabling requirements
Fault tolerant – handled entirely in hardware
  switches to single wire mode on fault
  switches back to normal mode on restoration of fault
Notes: Low-speed CAN is commonly used to control “comfort” devices in an automobile, such as seat adjustment, mirror adjustment, and door locking. It differs from “high-speed” CAN in that the maximum baud rate is 125K and it utilizes CAN transceivers that offer fault-tolerant capability. This enables the CAN bus to keep operating even if one of the wires is cut or short-circuited because it operates on relative changes in voltage. The fault tolerance feature means that communications capability is maintained even if any of the ISO11519 wiring failures occur. The transceiver solves many common and frequent wiring problems such as poor connectors, and also overcomes short circuits of either transmission wire to ground or battery voltage, or the other transmission wire. The transceiver resolves the fault situation without involvement of external hardware or software. On the detection of a fault, the transceiver switches to a one wire transmission mode and automatically switches back to differential mode if the fault is removed.

## Slide 12: NI-CAN Access to the CAN Bus
Object oriented architecture
CAN network interface object – CAN port
  Low level access to CAN bus
  When writing or reading you must specify the ID, data length, etc., of interest
CAN object – encapsulates a specific arbitration ID along with its data
  High level access
  At configuration time, you specify ID, data length, etc., of interest
Notes: NI-CAN uses object-oriented terminology and concepts.
Object-oriented terminology provides an excellent model for describing device networks in terms that are easy to understand.
In object-oriented terminology, the term class describes a classification of an object, and the term instance refers to a specific instance of that object. The term object is generally used as a synonym for instance. For example, NI-CAN defines a class called the CAN Network Interface Object, which encapsulates any network interface port on a National Instruments CAN hardware product. Specific instances of the CAN Network Interface Object are referenced with names like CAN0 and CAN1. Each instance of a particular class has attributes that define its externally visible qualities, as well as methods that are used to perform actions. For example, each instance of the CAN Network Interface Object has an attribute for the baud rate (bits per second) used for communication, as well as a method used to transmit CAN frames onto the network.
The CAN Object encapsulates a specific arbitration ID, along with its data. In addition to providing the ability to transmit and receive frames for a specific arbitration ID, CAN Objects also provide various forms of background access.

## Slide 13: NI-CAN – Network Interface Object
Useful CAN analyzer type of applications
Configuration of CAN ports
  Baud rate, queue length, comparators/masks
Time stamping of the incoming frames
Retrieve all arbitration IDs that fit to comparators/masks
Ability to do statistical analysis of the traffic on the CAN port
Notes: The CAN Network Interface Object encapsulates the entire CAN network interface. Its attributes are used to configure settings that apply to the network interface as a whole. For example, the CAN Network Interface Object contains an attribute you can use to set the baud rate that the network interface hardware uses for communication. The CAN Network Interface Object is used to communicate generically on the CAN device network. For example, you can use the write function to transmit a CAN remote frame to a pushbutton device, then use the read function to retrieve the resulting CAN data frame. Because the CAN Network Interface Object provides direct access to the network interface, the write and read functions require all information about the CAN frame to be specified, including arbitration ID, whether the frame is a CAN data frame or a CAN remote frame, the number of data bytes, and the frame data (assuming a CAN data frame).
The Network Interface can be configured to do a buffered acquisition in which its Read Queue is allocated to buffer high speed incoming data. Comparators masks can be used to retrieve Arbitration Id’s of interest otherwise all the data from the network is placed in the read queue. This feature is valuable in analyzer application in which it necessary to know which device are active on the network

## Slide 14: NI-CAN – CAN Objects
One object is one arbitration ID
Buffering of CAN frames per arbitration ID
Time stamping of the incoming frames
Predefined communication methods
  Automatic handling of cyclic remote transmission frames
  Periodic sending of single frames or even waveforms
Notes: The CAN Object encapsulates a specific arbitration ID, along with its data. In addition to providing the ability to transmit and receive frames for a specific arbitration ID, CAN Objects also provide various forms of background access. For example, you can configure a CAN Object for arbitration ID 13 to automatically transmit a CAN remote frame every 500 ms, and to store the data of the resulting CAN data frame for later retrieval. After the CAN Object is configured in this manner, you can use the read function to obtain a single data byte that holds the most recent state of the pushbutton.

## Slide 15: NI-CAN Existing Products
High speed CAN (ISO 11898)
  AT, PCI, PXI™/CompactPCI, PCMCIA
  1 and 2 ports
  Maximum baud rate 1Mb/s
Low speed CAN (ISO 11519)
  PCI, PXI/CompactPCI, PCMCIA
  1 and 2 ports
  Maximum baud rate 125kb/s
  Fault tolerant design

## Slide 16: NI-CAN New Products
RTSI support (NI-CAN 1.4)
  Synchronization with DAQ/IMAQ™ using RTSI
Dual speed CAN cards (NI-CAN 1.4)
  PCI, PXI/CompactPCI, PCMCIA
  1 port high speed and 1 port low speed CAN port
  Auto cable detection for PCMCIA

## Slide 17: NI-CAN Architecture
PC
  Your application
  NI-CAN language interface
  NI-CAN.DLL
CAN interface
Shared memory
CAN stack
CAN network
R
T
S
I
Notes: A 32-bit, multitasking aware device driver is used to interface with National Instruments CAN hardware. Under Windows 98/95, this is a dynamically loadable, Plug and Play aware virtual device driver (VxD). Under Windows NT, this is a native Windows NT kernel driver.
A Win32 dynamic link library, nican.dll, acts as the interface between all CAN applications and the NI-CAN device driver.
NI-CAN hardware products also have an on-board microprocessor. This microprocessor is used so that all time-critical aspects of the NI-CAN software can be executed separately from your Windows application. The firmware image (CAN stack) which runs on the on-board microprocessor, is loaded and executed automatically when your NI-CAN application starts up.

## Slide 18: Typical Applications
Torture testing of a gear box
Optimizing gear box development
Testing of CAN radar sensors for distance measurements
Testing an ABS system

## Slide 19: Example CAN Application
Gearbox test stand
CAN bus
Temp
Pressure
Torque
….
…..
0
8
CAN frames
PC
CAN
DAQ – controlling the test stand – “soft”
DAQ
DAQ synchronized with CAN - “hard”
Temp
P
T
T
Notes: The above test has the following features:
• 32 A/D channels with 500 Hz scan clock
• Displaying and logging of data in 1h files
• Synchronous sampling of CAN frames
• Triggering of A/D channels with CAN data
  • Gear shifts are signalled by a CAN frame
  • Every shift is a trigger event
  • Display 500 ms pre trigger and post trigger of A/D and CAN data for every shift

## Slide 20: Synchronization (Software)
Software timing, triggering
Non-deterministic, non real time
OS latencies play a major role
Sharing of common timing sources via software global variable
Manual correlation of data for charting and/or post analysis
Notes: As noted in slide 3, the physical quantity being measured by DAQ and CAN devices must be done as close together (synchronized in time) to correlate the data. This synchronization can be done in software, but the latency of the operating system introduces delays that may not be acceptable for some automotive test applications.

## Slide 21: Synchronization (Hardware)
Hardware timing and triggering
Very deterministic
No OS involvement (done on board)
Tighter integration of CAN, DAQ, IMAQ measurements
Easy and automated methods for correlating data for charting and/or post analysis
Notes: National Instruments CAN, DAQ boards are equipped with a Real Time System Integration (RTSI) bus that allows routing of timing/trigger signals between them.
In a system that is coupled using the RTSI bus, a CAN or DAQ board can be the Master, driving the timing/trigger signals while other DAQ or CAN boards are Slaves to this timing signal and base their actions on this signal. Since the RTSI timing signals are handled in hardware, the host software running on the PC, does not interact in the acquisition or transmission (other than retrieving the data when it has being acquired or writing new data).

## Slide 22: RTSI Synchronization
Need a RTSI cable for PCI, ISA boards
PXI includes RTSI signals in backplane
Easy configuration via attributes
8 lines available (0-7)
CAN board configurable as RTSI master or slave
Ability to use network interface or CAN objects
All functionality handled in hardware
Notes: Before beginning to use RTSI between CAN and DAQ, a decision has to be made as to which board should be used as the Master. NI-CAN software allows easy configuration of the Network Interface or CAN Objects as a Master or the Slave.
The software attribute that configures the object as a Master or Slave is the RTSI Mode. The following RTSI Modes are available in NI-CAN:
1. Disable RTSI
2. On RTSI Input - Transmit CAN Frame
3. On RTSI Input - Timestamp RTSI event
4. RTSI Output on Receiving CAN Frame
5. RTSI Output on Transmitting CAN Frame
6. RTSI Output on ncAction call
Modes 2 & 3 configure the object (Network Interface or CAN Object) as a Slave that takes an action on the RTSI signal.
Modes 4-6 configure the object (Network Interface or CAN Object) as a Master.

## Slide 23: DAQ as Master
Timestamp RTSI trigger on RTSI input (simultaneous acquisition of CAN frame)
  Useful in applications that need to be synchronized to a DAQ scan clock
Transmit CAN frame on RTSI input (analogous to CAN analog output)
  Useful in applications that need to be synchronized to a DAQ update clock
  Can transmit periodic (single frame and waveform) from CAN
Notes: With DAQ (or IMAQ) board as the driver of the RTSI signal, it is possible to :
1. Time stamp the RTSI event and log it to the Read Queue
2. Transmit a CAN frame on the RTSI event
If a DAQ board is used, it could be configured to do an AI or AO operation for each of the above modes. Hence the DAQ board could route the Scan or the Update clock to RTSI and the CAN board could either log this event to the Read Queue or transmit a frame.
This functionality is available for the Network Interface as well as CAN Objects. Some background modes are supported with RTSI. For example, a DAQ board could be loaded with a buffer of data values that constitute a sine wave. In a similar way, the Write Queue could be loaded with an identical waveform to be transmitted via the CAN device. Once the CAN object is configured to transmit waveform on RTSI, it will transmit whenever the update clock signal arrives on the configured RTSI line. Note that the application software interaction would be load another set of waveform data if necessary, otherwise the timing and transmission are all handled in hardware (real time)

## Slide 24: CAN Synchronization with DAQ (RTSI)
RTSI cable
RTSI cable
DAQ card drives synchronization event:
CAN card
DAQ card
node
node
node
Transmit CAN when DAQ sends RTSI
AI/AO
AI scan clock or
AO clock update
node
node
node
AI/AO
CAN card
DAQ card
Receive CAN when DAQ sends RTSI
DAQ 1
DAQ 2
DAQ 3
CAN1
CAN2
CAN3
…..
…..
LabVIEW memory
}
AI scan clock or
AO clock update

## Slide 25: CAN as Master
Output a RTSI trigger on receiving a CAN frame
  DAQ uses incoming RTSI signal as acquisition clock
Output a RTSI trigger on (sucessful) transmission of CAN frame
  Similar to analog output from DAQ
Output a RTSI trigger on demand
  Example – manual control via pushbutton
Notes: With CAN as a driver of the RTSI signal, it is possible to:
1. Output a RTSI signal on receiving a CAN frame
2. Output a RTSI trigger on (sucessful) transmission of CAN frame
3. Output a RTSI trigger on demand
A DAQ or and IMAQ board could use this trigger to either perform an acquisition or an output.

## Slide 26: CAN Synchronization with DAQ (RTSI)
CAN card drives synchronization event:
CAN card
DAQ card
RTSI cable
node
node
node
CAN message received
CAN card
DAQ card
RTSI cable
node
node
node
CAN message transmit
Ack
AI/AO
AI/AO

## Slide 27: Demo
RTSI synchronization with DAQ

## Slide 28: Demo
RTSI synchronization with IMAQ

## Slide 29: Questions?