## Slide 1: Experience the Power of FlexMotion™
Sundeep Chandhoke
Software Group Manager
Thurs Aug 17
10:15-11:30 a.m., 1:45-3:00 p.m.
Cedar (8C)

## Slide 2: NI-Motion High Performance Servo/Stepper Controller
Deterministic
Flexible
Machine vision
Machine monitoring
FlexMotion
Power to solve
applications
Easily
Faster
Cost effectively
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
FlexMotion is National Instruments high performance motion controller. It controls both servo and stepper motors.
FlexMotion integrates well with all National Instruments data acquisition and image acquisition products using the Real Time System Integration (RTSI) bus and easy to use NI-Motion™ software.
Using two processors, the FlexMotion controller is fast and highly deterministic. FlexMotion’s easy to use software helps improve the time to market for products and is cost effective.

## Slide 3: Architecture
Dual processor architecture determinism
Open architecture ease of use
FLASH memory architecture flexibility
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
FlexMotion controllers have a dual processor architecture. They connect to PCs and give you the best of both worlds – determinism and the ease of programming along with high performance embedded controllers.
The open architecture environment makes it easy to integrate FlexMotion with image acquisition and/or data acquisition to customize your application.
The FLASH memory architecture enables you to get firmware updates that provide new features with every NI-Motion software release. Both the firmware for the processors and the code that boots the Field Programmable Gate Array (FPGAs) can be updated.
If the controller is operated in stand-alone mode, an onboard program can be saved to non-volatile FLASH memory. This allows the board to come up and start executing motion applications as soon as it’s powered on. You can also save motion initialization parameters to FLASH memory and eliminate the need for further initialization.

## Slide 4: FlexMotion Block Diagram
Real-time OS
Host communications
Command execution
Motion sequencing
I/O reaction
System supervision
Trajectory
generator
Control
loop
D/A
Stepper
Feedback
Motion I/O
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The basic components of the FlexMotion controller are
1. supervisory control
2. trajectory generator
3. control loop
The supervisory control handles all the host communications, command sequencing and coordination.
The trajectory generator generates the motion profile on the fly (multiple axes).
The control loop simultaneously handles the fast, closed-loop control with position, velocity, and trajectory maintenance on multiple axes.
Motion IO handles all IO specific to motion such as breakpoint position, trigger inputs, homing, and limits.

## Slide 5: Architecture
PC
Microprocessor
running
real-time
operating system
FlexMotion device
DSP
FPGAs
Host computer
Encoders/
motion I/O
Control loop/
Trajectory generation
Supervision/communication/
User defined onboard programs
Offload the host computer
Reliable operation
Deterministic behavior
Notes: In addition to handling all communications, the microprocessor provides a reliable platform to run onboard programs.
Onboard programs offload the host computer and allow the motion part of your product to run reliably and deterministically. In addition, you can set up onboard programs to begin without interaction when the controller is powered on.
The real-time trajectory generation and control loop (enhanced PID) is handled by the DSP. This gives a second level of determinism. Even if the onboard microprocessor is busy handling communications and onboard programs, the trajectory generation and control loop calculations are not affected at all. This architecture ensures that the motion profiles are totally under control at any given time and condition.

## Slide 6: Applications
Pleating machine
Web cutting
Flying welding
High precision positioning devices
Notes: To understand some of the most powerful features of the FlexMotion device, let’s look at a few examples and see how these features of FlexMotion solve the application.

## Slide 7: Application 1 – Pleating Machine
Pleating machine
The upper and lower knife blades are moved in
circular motion to form the pleats
The web fed into the machine is to be
pleated
Makes cartridge filter elements and pleated filter bags used in the industrial filtration industry
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
JCEM’s revolutionary new NC Type computerized pleaters are for manufacturers of cartridge filters, element, and pleated filter bags in the industrial filtration industry. The NC pleater features programmable controls for the parameters of the total pleating job. At the touch of a button, adjustments can be made to the knife pleat heights to produce parallel vertical pleats on materials such as paper,polypropylene,polyester, nomex, ryton, HEPA,woven metal wire cloth, and other media.

## Slide 8: Pleating Machine – Requirements
Fully automatic and adjustable blades, electronically controlled and without control cam discs
Pleat height and working width needs to be customizable depending on the material used
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The NC Knife pleating machines are electronically controlled, fully automatic, adjustable without control cam operations, and can be used for the continuous production of pleated elements at a pleat height between 4 and 120 mm. Special pleat height and working width can be customized upon request. This is different from the standard pleating machine because it does not use cam discs for the knife movement.
The inclination and setting angle of the knife is an additional set-up parameter than can to optimize the knife movement accordingly to the demands for the different materials. The stroke movement of the folding knives is minimized and equivalent to the set pleat height. This results in an increase of pleat capacity, especially for the lower pleat heights (4 to 15 mm, of 150 pleats/min).

## Slide 9: Solution
FlexMotion features use
Onboard programming
  The motion application runs on the controller to move the blades deterministically and reliably
Circular interpolation and blending
  Blending circular interpolated moves creates the motion needed for pleating
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The following features on the FlexMotion controller implement the pleating machine:
Onboard programming – The onboard programming environment offers a reliable and deterministic platform for executing the motion profiles. The rate at which the material is pleated remains constant and is not effected by non-reliability of the Windows OS.
Circular interpolation – One of the main characteristics of the pleating machine is to make it without CAM discs and change the stroke and inclinations of the blades programmatically. This is achieved by using two servo motors along with the FlexMotion controller circular interpolation mode to control each blade.
Blending – To cause the material to be “pleated” two arc segments should be blended at different velocities. The trajectory blending feature offered by the FlexMotion controller makes this possible.

## Slide 10: Onboard Programs
Multiple program execution
Totally event driven
Onboard variables for data
synchronization
Create loops
Onboard Program
Wait for events
FlexMotion
Stop Event
Notes: You can store multiple programs and run on the FlexMotion controller simultaneously. Special onboard variables and functions synchronize onboard programs with each other and the host computer.
Onboard programs are entirely event driven.

## Slide 11: Writing an Onboard Program
Host
computer
Host Communication Handler
Begin store #
End store #
FLASH
RAM
Memory
Object memory
management
FIFO
Save/delete
Free
Any function
FlexMotion running RTOS
Save to RAM
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Using the “Begin Store” and “End Store” functions, onboard programs can be saved to RAM. To save or delete these programs to non-volatile FLASH, use the “Object Memory Management” function.

## Slide 12: Onboard Program Execution
Trajectory generator
Host
computer
Host communication handler
Event handler
Onboard program (1)
Run program #
FlexMotion running RTOS
Onboard program (2)
Onboard program (3)
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
When you save a program in volatile or non-volatile memory on the 68331, then on executing the “run program” function causes the host communication thread to spawn a thread and running the onboard program.
The onboard program can execute the same functions that you can execute from the host computer. In addition, there are special functions that allow you to create loops to sleep and manage onboard variables.
Using the “wait on condition” function you can make the onboard program go to sleep and only wake up during a specified condition. Once the condition occurs, the event handler thread wakes the onboard program as it continues to execute it’s functions.

## Slide 13: Circular Interpolation
Trajectory
generator
Cubic spline
Radius
Length of arc
Velocity
Acceleration
Deceleration
Cubic splining guarantees low jerk and smooth arcs
Notes: Creating a circular profile is easy in FlexMotion. Simply indicate the radius and the travel length of the arc. The FlexMotion controller’s trajectory generator then produces points based on constraints such as maximum velocity, acceleration, and deceleration. These points are then interpolated using a cubic spline algorithm, which results in smooth arcs with low jerk and no chordal error.

## Slide 14: Contouring
Cubic spline
Positions
N milliseconds
apart
Cubic splining allows customized profiles
Notes: Customized trajectory profiles can be created using the splining algorithm in FlexMotion. If points are transferred to the FlexMotion controller “N” milliseconds apart, the controller can directly spline these points to generate user defined trajectory profiles without using the internal trajectory generator.

## Slide 15: Blending
Combine motion profiles by superimposing trajectories
Controllable superposition point
Move 1
Move 2
Time
Velocity
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The segments blend with two trajectory generators and compile instantaneous position command outputs before going to the PID or stepper control block.
The trajectory profiles are effectively combined by linear superposition.
Any two move segments can be blended – straight line into another straight line, straight line into an arc, arc into another arc, or arc into straight line.
This works with vector move segments or even single axis segments.
Typically, start the second move when the first move starts to decelerate (blend factor is -1) as shown in this slide.

## Slide 16: Blending
Combine motion profiles by superimposing trajectories
Controllable superposition point
Move 1
Move 2
Time
Velocity
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Segments can blend when first trajectory comes to a complete stop (blend factor = 0).

## Slide 17: Blending
Combine motion profiles by superimposing trajectories
Controllable superposition point
Move 1
Move 2
Time
Velocity
Delay
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Segments can also blend after a programmable delay (blend factor = delay in milliseconds).

## Slide 18: Application 2 –Web Cutting
Web
Knife
Rotating knife is used for cutting a web of paper or plastic
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The web is advanced at constant speed while the knife is rotating. The objective is to cut the web at intervals of specified length.

## Slide 19: Web Cutting – Requirements
Blade and web velocity must match at cut
Vary the cut length
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
As the knife is geared to the web it is synchronized. This results in a cut equal to the circumference of the blade path. The cut length may be modified by adjusting the speed of the knife. During the interval the knife is not in contact with the web. This is done by super-imposing a trajectory on the rotating knife.
Sometimes the Web is elastic and can stretch under tension. When this happens the web is marked once per cycle at the required cutting location. This mark reads as a high speed capture input, which makes the knife’s motion controller adjust the speed .

## Slide 20: Solution
FlexMotion features used –
Electronic gearing
  Ensures speed of the blade – speed of web
Superimposed moves
  Controls size of cut
High-speed capture (trigger input)
  Synchronizes blade with the web
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The following features on the FlexMotion controller implement the Web Cutting application –
Electronic Gearing – This feature ensures that the speed of the blade is equal to that of the web when the blade meets the web
Superimposed Moves – Superimposing moves on the moving blade reduces or increases the length of the cut.
High Speed Capture – A trigger input to the FlexMotion controller causes the position of the blade to be captured and accordingly superimpose a move on the blade to control the length of the cut

## Slide 21: Electronic Gearing
One motor (slave) is driven in proportion to position on another motor or feedback device (master)
Advantages over mechanical gears
  Flexibility – can change gear ratios any time
  Combined motion – second motion profile over geared motion
Absolute/relative gear ratios
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The master position can come from any encoder or analog input channel. The encoder can be the feedback for a controlled master axis or an independent position sensor used to monitor an uncontrolled axis. It can also be the output of the master axis trajectory generator. Using the trajectory generator’s output improves tracking by eliminating the master’s following error.

## Slide 22: Electronic Gearing
Every update period –
Slave position = gear Ratio x master position
For superimposed moves, every update period –
Slave position = (gear ratio x master position) + (position from trajectory generator of slave)
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Master/slave gearing does not directly use a trajectory generator – the slave’s instantaneous position is simply the master’s instantaneous position multiplied by the gear ratio. Since the slave’s trajectory generator is free, it can be used to superimpose a move on the slave axis.
The typical use of a superimposed move is for registration. FlexMotion controllers have high-speed position capture circuits and a relative-to-capture position mode that specifically supports registration applications.

## Slide 23: High Speed Capture
An external trigger captures the position
The relative to capture mode allows an axis to move to the captured position
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
An external trigger on the FlexMotion controller can cause the encoder FPGA to capture the position of an axis at the instant the trigger occurs (100 nanosecond accuracy). The axis then can be commanded to move relative to the captured position.

## Slide 24: Application 3 – Flying Welding
The objective is to weld two spots four inches apart. The first spot is two inches from the leading edge.
The Welding is performed while the parts are moving.
Welding Head
Encoder connected to FlexMotion
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The objective is to weld two spots four inches apart. The first spot is two inches from the leading edge.

## Slide 25: Flying Welding – Requirements
Welding should occur while the parts are moving – “on the fly”
The welding head should orient itself based on the leading edge of the part
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The welding must happen while the parts are moving on the conveyor. Also, the welding gun must orient itself depending upon the initial edge of the part.

## Slide 26: Solution
FlexMotion features used
Electronic gearing
  Maintains the speed of the welding edge equal to the rate at which the part is moving
Relative gear ratios
  Changes the speed of the slave causing it to perform the two welds two inches apart
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
A sensor detects the leading edge of the moving part and sends a high-speed trigger to the FlexMotion controller.
The FlexMotion controller enables gearing (ratio 2:1) to place the welding gun two inches from the leading edge. After a pre-determined time interval, the gear ratio becomes 1:1 and welding is performed.
After a time delay the gear ratio is changed 0:1, which causes the slave (welding gun) to stop. Once the welding gun is in position for the second weld, the gear ratio is re-enabled 1:1 to make the second weld.
After the second weld is over, the controller disables gearing and moves the welding head to the starting position where it waits for the next part to arrive.

## Slide 27: Application 4 – High Precision Positioning Devices
Retrofit precision milling machines
Hard disc drive manufacturing machines
Precision flight motion simulators
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Certain applications need a high degree of precision.
Milling is a machining operation that occurs when a work piece performs linear movements and takes the shape of a rotating cutter. High precision milling machines need very high positional accuracy.
Hard disc drive manufacturing machines need to operate at high speeds and eliminate almost all jitter.
Flight motion simulators test inertial measurement units, inertial navigational systems, and gyroscopes in closed gimbal configuration.

## Slide 28: High Precision Positioning Devices – Requirements
Accuracy up to 1/10000 of an inch
High speeds above 200 inches/sec
Minimization of backlash
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
High precision devices require high positional accuracy at high speeds. As most of these systems use mechanical gears (linear or rotary), the effect of backlash on the system is minimized to ensure a stable system.

## Slide 29: Solution
FlexMotion features used–
Dual-loop feedback
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Dual-loop feedback in FlexMotion gives the desired accuracy and precision that these systems (such as precision milling machines) need.

## Slide 30: Dual-Loop Feedback for Enhanced Stability and Precision
Two position sensors One on motor One on load
Motor position sensor Damping to stabilize the loop (velocity feedback)
Load position sensor Position feedback
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Two feedback sensors are required to implement dual-loop feedback. Each axis in the FlexMotion controller can configure the use of two feedback devices. The control loop can then use the two position sensors to ensure high positional accuracy and stability.

## Slide 31: Dual-Loop Feedback


System
I/N
B
Load sensor
Motor sensor
Kp and Ki
R +
C -
Position Feedback
Velocity feedback
Backlash
Mechanical gear
Kv
E
R - Set point
C – Current position
E - Position error
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
Backlash affects system stability and precision. The purpose of the “Kd” term in the PID loop is to estimate the velocity of the motor by differentiating the position error. This term dampens the stability of the loop. If backlash is present between the motor and position sensor, the positions of the motor and the sensor are no longer the same. This difference in position causes the derived sensor velocity to be sufficiently different than the motor velocity. This becomes ineffective for damping purposes and eventually leads to system instability. The dual loop feedback approach helps increase system stability and reduce instability caused by backlash.
The dual loop scheme uses two sensors. The motor sensor provides velocity feedback, while the load sensor provides position feedback. The mix of these two signals provides the correct feedback for damping and stability. This helps increase the precision achieved by the controller.

## Slide 32: Conclusion
Creating an application with FlexMotion is –
Easy
Powerful
Fast
Cost effective
Notes: WS2C– <number>
Experience the Power of FlexMotion
<header>
<date/time>
The architecture of FlexMotion makes it powerful and easy to use.
Most complex applications are easily solved using the FlexMotion controller and NI-Motion software.
The dual processor architecture of FlexMotion, with re-configurable firmware and FPGAs makes it one of the most powerful and flexible controllers in the market today.