## Slide 1: Taking Advantage of IVI™ Simulation in Measurement Studio™
Dany Cheij
Product Manager
Thurs Aug 17
12:00-1:15 p.m., 3:30-4:45 p.m.
Cedar (8C)
Notes: Thank you for joining us for this workshop on IVI or Interchangeable Virtual Instruments. This workshop covers the Simulation capabilities of IVI and how to use them in Measurement Studio.

## Slide 2: Agenda
IVI background
IVI architecture
IVI benefits
IVI simulation
  Class vs. specific-level simulation
  Interactive vs. programmatic simulation
  Custom simulation drivers
Questions
Notes: In this workshop, we give a brief background of IVI and an update on the IVI Foundation which is the governing body of the IVI specification. We then give an overview of the IVI architecture and discuss National Instruments implementation of that architecture. Then we discuss some of the benefits of IVI such as state caching and interchangeability.
The bulk of the workshop is devoted to a discussion on IVI simulation and the different tools available in Measurement Studio to take advantage of that simulation. We show the difference between specific driver level and class driver level simulation, and interactive and programmatic simulation. Finally, we discuss how you can use custom simulation drivers in your programs.

## Slide 3: What is IVI?
IVI Foundation announced in August 98
Charter – define standard programming interface for instrument drivers
Define instrument driver specifications:
Instrument Class (e.g., IviDmm)
Driver Capabilities
Base Capabilities (Required): e.g., Measure DC Voltage or DC Current
Extension Groups (Optional): e.g., Measure Temperature
Vendor-Specific Capabilities (Optional):
e.g., Trigger at User-Specified Threshold
Notes: In early 1997, National Instruments was approached by several instrument end-user companies interested in developing a new standard for instrument drivers built on existing approaches, such as VXIplug&play, and that addressed several concerns such as instrument state-caching, simulation, and interchangeability.
As a result of those discussions, a group of nine companies formed the Interchangeable Virtual Instruments or IVI Foundation. The charter of the Foundation is to define a standard programming interface for instrument drivers while allowing instrument interchangeability, regardless of instrument manufacturer or I/O bus interface.
The Foundation is developing these standards by identifying common instrument types such as digital multimeters or oscilloscopes, and then identifying a common set of features within each instrument type and dividing these features into three groups – base capabilities, extension capabilities, and vendor specific capabilities. The Foundation then develops a set of specifications for each of these instrument types, and defines a corresponding instrument class specification.
For example, in the digital multimeter (DMM) class the base capabilities include making DC voltage and DC current measurements, the extension groups include making temperature measurements, and the vendor-specific capabilities include triggering at a user-specified threshold.

## Slide 4: IVI Foundation Update
Current classes:
  Multimeter (DMM)
  Oscilloscope
  Switch
  Arbitrary waveform/ function generator
  DC power supply
50 companies
Future classes:
  RF signal generator
  Spectrum analyzer
  Power meter
  Digital instruments
C and COM-based architectures
Notes: Since its founding in August of 1998, the IVI Foundation has been working on revising the specifications for the five instrument classes that were initially defined. Revision 2.0 of the following class specifications were completed and subsequently voted on and approved by the Foundation membership in December of 1999 – digital multimeters, oscilloscopes, switches or matrices, arbitrary waveform or function generators, and DC power supplies.
In addition, the Foundation’s membership roster has been expanding steadily from nine founding members to more than 50 current members. The membership includes end-user companies, systems integrators, as well as all major instrument and software vendors, including National Instruments, Agilent Technologies, Tektronix, and Rohde & Schwarz.
With the experience of developing and revising the first set of instrument classes, the Foundation has now turned its attention to defining new instrument class specifications such as RF signal generators, spectrum analyzers, power meters, digital instruments, and AC power supplies. In addition, the Foundation will look into defining interfaces for the latest in software component technology, starting with the current drive to define a COM interface.

## Slide 5: IVI Overall System Architecture
IVI defines a two-tiered architecture for drivers:
  Instrument-specific drivers – performance improvements
  Generic class drivers – interchangeability
Builds on VISA or other standard I/O library
Can develop non class-compliant drivers
Test Program
Hardware
I/O Library
(VISA or other)
IVI Specific Driver
IVI Class Driver
IVI Specific Driver
Notes: The IVI Foundation defined an architecture for its drivers that is hierarchical and layered in nature and that leverages industry-standard technology. This architecture fits into a complete modular system from National Instruments. The test program uses IVI drivers for the instrument communication. The IVI layer in turn uses an industry-standard I/O library such as VISA to communicate with the hardware that is in the system, regardless of whether it is GPIB, VXI, PXI™ or computer-based instrument hardware.
The IVI layer itself is divided into two sub-layers. The lower is the IVI-specific driver layer. These are instrument-specific drivers that are intended to be used with specific instrument models, and they are designed to provide the performance improvements of IVI, such as state-caching, multithreading, and simulation.
The upper sub-layer is the IVI class driver layer. These are the generic class drivers that you can use in conjunction with specific drivers to control any instrument in a class. This layer provides the interchangeability benefit of IVI.
The IVI specs also allow drivers to be created for instruments that do not fall into one of the IVI defined classes. Users can develop specific drivers to take advantage of performance benefits or define their own instrument class.

## Slide 6: Specific Driver vs. Class Driver
Specific drivers:
  One driver per instrument
  New features (state- caching, simulation, range-checking)
  Specific functions:
    niDmm_init,
    tktds2x0_ReadWaveform
    hp33120a_close
Class drivers:
  One driver per instrument class
  Interchangeability and advanced simulation
  Generic functions:
    IviDmm_init
    IviScope_ReadWaveform
    IviFgen_close
Notes: Specific drivers are very similar to traditional drivers in many ways. Each instrument has one instrument driver composed of high-level functions that make it easier to programmatically control the instrument. Each instrument driver includes features such as state-caching, simulation, and multithreading. All functions within a driver have the same prefix to identify that driver. For example, niDmm_init, hp33120a_GenerateWaveform, tktds2x0_close.
Class drivers provide the interchangeability of IVI. There is one driver for each class of instrument and it contains functions with generic names, such as IviDmm_init, IviFgen_GenerateWaveform, and IviScope_close. Each function maps to a function within the specific driver. When the class driver is used within a program, each high-level function calls the appropriate function within the specific driver being used at the time. By using these drivers, the user can switch the instrument being used by swapping specific drivers without having to rewrite any code or recompiling their program. In addition to interchangeability, class drivers provide advanced simulation capabilities.

## Slide 7: NI IVI Internal Architecture
Test Program
(LabVIEW, LabWindows/CVI, VB, VC++ etc)
Instrument Driver Code
High-Level Programming API (for ease-of-use)
VISA
Standardized Attribute Model
State Cache
State
Management
Library
(Engine)
Notes: Let’s look a little closer at the internal architecture of a National Instruments IVI system. Traditionally, instrument drivers provided high-level function calls that could be called from test programs developed in LabVIEW™, LabWindows™/CVI, Visual Basic, Visual C++, and so on. From a user’s perspective, IVI drivers look exactly the same as these traditional drivers, with high-level functions such as Initialize, Configure, Measure, and so on. The difference in IVI is the new internal architecture that is used to communicate with the instrument.
IVI instrument drivers expose a high-level application programming interface (API) that you can use from within a test program written in LabVIEW, LabWindows/CVI, etc. This API accesses the internal driver code which uses a standardized attribute model to read or write the values of instrument attributes. In addition, IVI uses the National Instruments IVI Engine to maintain the state of the instrument in a software cache and optimize its performance. Finally, the instrument driver communicates with the hardware using the industry-standard VISA I/O library.

## Slide 8: IVI Benefits – State Caching
State of instrument tracked in software
Does not send redundant I/O across bus
Reduced command parsing time and increased efficiency
State Cache
Notes: The first IVI benefit we discuss is state-caching. It is a powerful mechanism used to keep track of the state of the instrument in software. The IVI state-caching engine remembers the state of the instrument and only sends the commands necessary to incrementally change that state, minimizing bus traffic to and from the instrument. Because state caching minimizes the number of commands sent to the instrument, overall bus bandwidth is increased reducing the time required to take measurements.
Although we have only highlighted state-caching, IVI drivers include other performance and development enhancements, such as range checking, interchange checking, spying, and multithread support.

## Slide 9: State Caching – How It Works
Instrument settings defined as attributes
Attributes set individually or as part of high-level function
Simple model for preserving state (attribute values)
  Attribute values dynamically cached when user sets value
  Attribute values either known (valid) or unknown (invalid)
  Attribute values can be invalidated
IVI Engine
Caching
“Is state-caching on?”
Compare 5.0 against
value of AMP in cache
If different, update
If same, return
cached
values
On/Off
SetAttr (AMP, 5.0)
IVI Driver
Send cmnd, or Proceed
Notes: In order to implement this state caching mechanism, IVI defines an attribute model. Each instrument setting is defined as an attribute, and the IVI Engine keeps track of the values of those attributes. You can set attributes individually, or as part of a high-level driver function.
You use this model to preserve attribute values. The first time a user sets the value of an attribute, the IVI Engine sets that value in the cache. The next time the attribute needs to be set, the new value is compared against the one in the cache and communication with the instrument only occurs if the two values are different. When the communication is completed, the value in the cache is reset. Attribute values in the cache can be invalidated. For example, Attr1 and Attr2 might be related and setting the value of Attr1 can invalidate Attr2.
The example on the slide shows the attribute model in work. Let’s say a user is trying to set the value of the AMP (Amplitude) attribute either directly or by calling the Measure function. The IVI driver tries to set the Attribute AMP to 5.0. The IVI Engine then determines if state-caching is on. If it is, the engine compares the value being passed to the value of AMP in the cache. If the attribute is valid and it is equal to 5.0, the engine stops and the program continues with the next command. If the attribute is invalid, or if it is not equal 5.0, the value in the cache is updated and the driver is instructed to send the command to set AMP equal to 5.0.

## Slide 10: IVI Benefits – Interchangeability
Swap hardware between:
  Instrument manufacturer (e.g., NI and Agilent)
  Communication bus (e.g., GPIB and PXI)
Protect software investment when hardware needs to be repaired or replaced
Share software between units using different hardware
Test Program
(LabVIEW, CVI, VB, VC++ and so on)
Fluke 45 or NI 4060
DMM Class Driver
Notes: The next benefit of IVI we discuss is interchangeability. By developing software using the generic IVI class drivers, you can exchange any of the hardware in a system regardless of the instrument manufacturer, such as National Instruments or Agilent Technologies, or the instrument communication bus interface, such as GPIB, VXI, PXI, or serial.
The flexibility to exchange hardware provides the developer with the protection of their software investment should the hardware break down and need to be repaired, or become outdated and need to be replaced. Users can share software between units that might have different hardware in house, such as the development lab and the production floor.
Interchangeability gives the developer the flexibility to choose the hardware with the best performance and cost combination without having to worry about rewriting their software.

## Slide 11: Interchangeability – How It Works
User Application
(LW/CVI, LabVIEW, VB, VC++, etc)
NI 4060
Keithley 2001
Fluke 45 Specific Driver
Direct Access
NI 4050
Keithley 2001
Fluke 45 Specific Driver
DMM Class
Driver
Class Driver
NI 5112
HP 54645
Tek TDS 210 Specific Driver
Scope Class
Driver
Both
Notes: Interchangeability is implemented by providing a generic class driver with instrument independent functions. These functions have a generic function prefix such IviScope, IviDmm, or IviFgen. By using these generic functions the program code does not have to be changed when a user changes the hardware being used in their system.
When used in an application, these functions determine which instrument is being used by checking the IVI configuration file, and calls the corresponding function in the specific driver dynamically. The specific driver then issues the appropriate instrument communication commands and returns control to the class driver, which continues with the next function call.
The available functions are based on the IVI Foundation specs and might not cover all of the functionality of a specific instrument. As a result, the IVI architecture allows the user to make calls to the specific driver and the class driver in the same program.

## Slide 12: IVI in NI ADEs
Measurement Studio
  LabWindows/CVI
    Function panel files for drivers
  ComponentWorks™ – tools for Visual Basic
    Dynamic link libraries and ActiveX controls
  Tools for Visual C++
    Dynamic link libraries
LabVIEW
  Drivers as VI libraries
Notes: Before we discuss simulation and get into the main part of this presentation, we present the IVI support in the three components of Measurement Studio.
All IVI instrument drivers are currently available as dynamic link libraries (DLLs) with a type library for easy access. In LabWindows/CVI, IVI drivers also have a function panel file for easy access and navigation through the functions. In addition, the drivers use the same structure and contain some of the same functions as traditional instrument drivers which should be familiar to most users. LabWindows/CVI also ships with an IVI driver development wizard and a driver development guide.
IVI is also part of the ComponentWorks tools for Visual Basic (VB). In addition to being able to very easily call the DLLs from VB, ComponentWorks includes ActiveX controls for the two most popular IVI instrument classes – scope and DMM.
Finally, Measurement Studio tools for Visual C++ can also easily call the IVI DLLs.

## Slide 13: IVI Benefits – Simulation
Understand and test instrument functionality
Multiple developers share same hardware
Can use different hardware in production and development modes
Generate user-defined data and errors
Turn off Instrument!
Unplug Cable!
Program Simulating!
Notes: Another very important benefit of IVI, and the main topic of this workshop is instrument simulation. Simulation can be very useful in many different situations such as when you want to develop code for an instrument to understand its functionality and verify that it will perform the required operations before purchasing the instrument. It can also be useful when multiple users are sharing the development load and the hardware they are using is very expensive. In that case, having a separate set of hardware for each developer might be financially prohibitive. Also, in some applications the development environment and the production environment might using different hardware. With simulation, you can test the application with the new hardware before deployment to the production floor. Finally, simulation allows users to generate user-defined data and error conditions.

## Slide 14: Why is Simulation Needed?
With traditional implementation, at Init time
  Driver sends initialization command to instrument
  Instrument readies for remote communication
  Driver generates a unique software handle for use in subsequent driver calls
If instrument is not present at Init time
  An error is generated
  An invalid handle is returned
  All subsequent driver calls fail
Notes: The main need for instrument simulation occurs at initialization time. With traditional instrument driver implementations, when the initialization function call is made, the driver sends the appropriate initialization command to the instrument. The instrument then is initialized and readies itself for remote communication. The driver then generates a unique software handle for use in subsequent driver calls. The handle is just a unique integer value that identifies the current communication session.
However, if the instrument is not actually present at initialization time, the instrument communication fails, a driver error is generated and an invalid instrument handle is returned. As a result, because each subsequent driver function calls needs that handle as an input, all of those function calls also fail.

## Slide 15: How is Simulation Implemented?
At Init time, IVI drivers check simulation status
  If simulation is enabled:
    Driver does not communicate with instrument
    Driver generates a valid instrument handle
  If simulation is disabled:
    Driver communicates with instrument
On subsequent driver calls
  Driver simulates function’s intended behavior
    e.g., configuration, measurement, etc.
Notes: IVI solves this problem by checking whether the driver is in simulation mode at initialization time. If the driver is, it does not communicate with the instrument and generates a valid instrument handle for use in subsequent calls. Because no communication occurs, no error is generated if a physical instrument is not present. If simulation is disabled, the driver sends the appropriate initialization code to the instrument which in turn readies itself for remote communication and a valid instrument handle is generated. In each subsequent function call, the driver uses the session handle (whether generate through simulation or actual instrument communication) and uses the same logic to determine whether to communicate with the instrument or simulate the function’s behavior, such as configuring the instrument or taking a measurement.

## Slide 16: Enabling IVI Simulation
Enable simulation through Measurement & Automation Explorer
Enable simulation programmatically by setting IVI_ATTR_SIMULATE attribute
Notes: Enabling IVI simulation is very simple. It can be done in one of two ways:
You can enable it through the Measurement & Automation Explorer (MAX). If you open up the properties page of any defined IVI virtual instrument and switch to the Inherent Attributes tab, you see a Simulation checkbox. Select that checkbox if you would like to enable simulation. You also notice a dialog selection for determining the source of output data simulation. You can select either Class Driver level simulation or Specific Driver level simulation.
You can also enable simulation programmatically by setting the value of the IVI_ATTR_SIMULATION attribute to VI_TRUE. You can then also set the value of the IVI_ATTR_USE_SPECIFIC_SIMULATION attribute to VI_TRUE in order to use the more basic Specific Driver level simulation.

## Slide 17: Specific Driver Simulation
Permits usage with no instrument present
Performs range checking
Simulates basic data: e.g., sine wave for IviScope, random value for IviDmm
Source code provided for customization of data and simulated behavior
Can be implemented in non-class compliant IVI drivers
Notes: IVI offers two levels of simulation – basic simulation at the instrument-specific driver level and advanced simulation at the class driver level.
Instrument-specific simulation provides the developer with the ability to communicate with the instrument as if it was physically connected to the computer. Its most important task is to simulate the instrument at initialization time so the user can call other functions within the same driver. In addition, with instrument-specific drivers the user can simulate data that is returned by the instrument, and usually just return random data. National Instruments provides the source code for IVI specific drivers so they can be customized. As mentioned before, simulation can be implemented in non-class compliant IVI drivers.

## Slide 18: Class Driver Simulation
Allows advanced simulation of data, status codes, and VXIpnp functions
Notes: Class driver simulation is more advanced and in addition to simulating the instrument handle, the user can simulate returned data more accurately by returning specific waveforms and very precisely controlling the parameters and properties of those waveforms. In addition, the user can simulate the results of VXIplug&play functions, such as the Revision Query or Self Test functions. Finally, the user can simulate status code returns for certain driver functions to determine whether his/her code properly checks for errors.

## Slide 19: First Demonstration
First demonstration shows:
  How to communicate with an instrument using IVI
  How to enable IVI simulation
  How to simulate instrument at specific driver level
  How to simulate instrument at class driver level
Notes: In this first demonstration, we show how to use IVI drivers in a program and communicate with an instrument. We then enable simulation and show how to simulate an instrument’s presence first using specific driver simulation and then class driver simulation.

## Slide 20: Second Demonstration
Second demonstration shows:
  How to use IVI simulation in Visual Basic
  How to use IVI ActiveX controls in Visual Basic
  How to modify interactive simulation parameters
Notes: In this second demonstration, we show how to use IVI simulation in a Visual Basic program. We use the ComponentWorks – a component of Measurement Studio™ – ActiveX IVI controls to communicate with a scope and then enable simulation at the class driver level. We also show how you can interactively control simulation parameters and simulate Status Codes and VXIplug&play function calls.

## Slide 21: Advanced Interactive Simulation
Interactive simulation enabled by default
Simulation panel at Initialization and Measurement time
Set output data, function status codes, and VXIplug&play function responses
Unselect “always prompt for output data simulation” checkbox to finish execution with current values
Notes: As we saw in the previous demonstrations, when using IVI class-level simulation, an interactive simulation panel pops-up at initialization time and every time a measurement function is called. Interactive simulation is enabled by default. In the interactive simulation box, you can customize the data that you want returned to your program, you can customize the responses to VXIplug&play functions, as well as define certain status codes that are associated with individual driver function calls. In the top left corner of the simulation dialog is a checkbox labeled “allows prompt for output data simulation”. If that box is unchecked, the program will proceed and will always use the data that was last defined in the simulation panel.

## Slide 22: Non-Interactive Simulation
Set INTERACTIVE_ SIMULATION to VI_FALSE in class simulation driver default setup
  Program executes without user input
  Default data unless set in Default Setup
  No status codes and default VXIpnp simulation if not set in Default Setup
Notes: In addition, you are able to completely disable interactive simulation so the program executes without requiring input from the user. From MAX, if you open the Simulation Virtual Instrument Properties panel and switch to the Default Setup tab, one of the attributes that you can set is INTERACTIVE_SIMULATION. By default, it is set to True. To disable interactive simulation, set this attribute to False.
Once you complete that ask, your program can execute without user input. In the Default Setup tab, you can also specify status codes for all driver functions by modifying the status value for the corresponding attribute, and you can also modify the returned value and the returned status for the VXIplug&play functions.
In addition, you can insert attributes for the output data simulation parameters and define their values, keeping in mind that most of these attributes will be channel-based and will have to be set on a per channel basis. For example, if you wanted to set the frequency on Channel 1 to 10kHz and on Channel 2 to 20kHz, you would add the following functions to the Default Setup:
  FREQUENCY CH1 10000
  FREQUENCY CH2 20000
Please note that in the Default Setup tab you can omit the NISSCOPE_ATTR_ prefix that is part of the attribute names.

## Slide 23: Programmatic Control of Simulation
Programmatically control simulation parameter values
  Obtain simulation session handle
    Ivi_GetAttributeViSession(handle, “”, 0, &simSession);
  Using simulation session handle to set simulation parameters
    Ivi_SetAttributeViReal64 (simSession, "CH1", NISSCOPE_ATTR_FREQUENCY, 0, freq)
Allows more control and does not affect execution flow
Notes: You can programmatically control these simulation parameter values as well. The first thing you need to do is to obtain the simulation session handle. You can do this by using the following function:
  Ivi_GetAttributeViSession(handle, “”, 0, &simSession);
Where handle is the I/O handle returned at initialization time, and simSession is a variable that is declared as a ViSession.
Once you have this handle, you can set all of the simulation parameters that you set in the Default Setup tab. For example, to set the frequency of the returned data to the values described on the previous slide, you would call the following two functions:
  Ivi_SetAttributeViReal64(simSession, “CH1”, NISSCOPE_ATTR_FREQUENCY, 0, 10000);
  Ivi_SetAttributeViReal64(simSession, “CH2”, NISSCOPE_ATTR_FREQUENCY, 0, 20000);
With this method, you have great control over the data and status code simulation but does not affect the flow of the program execution.

## Slide 24: Simulation Data Sources
Other sources of simulation data
  ASCII text file
  Database file
  DataSocket™ server
Notes: In addition to setting the values of the simulation data through Default Setup or programmatically as described in the previous two slides, you can also setup your program to retrieve simulation data from a predefined source such as an ASCII text file, a database file, or even from a DataSocket server on a network. Through this process, you have much greater control over what data gets returned to your program and in what order.
DataSocket is a National Instruments technology that implements an easy-to-use, high-performance programming tool that is designed specifically for sharing and publishing live data in measurement and automation applications.

## Slide 25: Third Demonstration
Third demonstration shows:
  How to disable interactive simulation through simulation driver’s default setup
  How to set simulation parameters through simulation driver’s default setup
  How to programmatically modify simulation session parameters
Notes: In this third demonstration, we show how disable interactive simulation and how to set the values of simulation parameters through the class simulation driver’s Default Setup. We then show how you can programmatically modify the simulation session parameters and override the values in Default Setup.

## Slide 26: Advanced Interactive Simulation
Use interactive simulation with custom driver
Notes: If the simulation levels that we have seen so far are not suitable for your application or if you require additional customization and control over your simulation, you are able to create a custom simulation driver.

## Slide 27: How Can You Implement?
Three ways to customize simulation driver:
  Customize user interface only
  Customize driver behavior only
  Customize both user interface and driver behavior
Once customization complete:
  Compile new simulation driver DLL
  Link Simulation Virtual Instrument to new DLL
Notes: There are three ways that you can customize your simulation driver – you can customize the user interface, the driver behavior, or both. Once the customization is complete, you compile the new driver into a dynamic link library (DLL), and link your Simulation Virtual Instrument to the new DLL.

## Slide 28: Customizing User Interface
Copy files from C:\VXIpnp\WinXX\niivi\sim
Modify appropriate .uir file
  e.g., nisscopu.uir, nisdmmu.uir, etc.
Customize controls and chart
  Modify control type, behavior, and default values
  Keep existing constant names
  Recompile simulation driver DLL
Notes: The most basic thing you can customize is the user interface of the simulation driver. All of the necessary files are in the C:\VXIpnp\WinXX\niivi\sim directory (XX=NT or 95 depending on the operating system). You then modify the appropriate user interface file (.uir) such as nisscopu.uir or nisdmmu.uir Once you open one of these files, you can modify the control types, behavior and default values. You should make sure that you keep the existing constant names for all the controls, unless you intend on modifying the corresponding .c file as well. You will then recompile the simulation driver DLL or create a new one.

## Slide 29: Customizing Driver Behavior
Copy files from C:\VXIpnp\WinXX\niivi\sim
Modify appropriate .c & .h files
Customize returned data
  Update waveform parameters
  Add waveform types
Customize driver timing
  Simulate instrument behavior
Notes: You can also customize the driver’s behavior. This would entail modifying the appropriate .c and .h files, which can also be found in the C:\VXIpnp\WinXX\niivi\sim directory (e.g., nisscope.c & nisscope.h). You can customize the returned data type and values as well as the driver timing. By default, the simulation driver executes as fast as the host computer allows and does not closely mirror the behavior of the actual instrument. You can add timing delays into each function in the driver to more closely match the behavior of the instrument while responding to that function.

## Slide 30: Compiling Custom Driver
Create LabWindows™/CVI project
Add appropriate files to project
Customize the necessary files
Set target as DLL
Select .h file as Export, and build DLL
Notes: In order to compile the new driver, you have to follow these steps:
Create a new LabWindows/CVI project.
Add all the necessary files to the project. These will always include nisimu.uir, nisimu.h, nisprefix.c, and nisprefix.h, where prefix is the name of the instrument class such as scope, dmm, or fgen. In addition, for the classes that support output data simulation (scope, DMM, and DC power supply), you need to add nisprefixu.uir and nisprefixu.h
You then customize the appropriate files according to the discussion in the previous slides.
You then make sure that you have set the target of the project as a DLL.
Finally, you will select the appropriate .h file as the Export for the DLL and proceed with building that DLL.

## Slide 31: Using Custom Driver
Update MAX configuration to use new DLL
  Update existing simulation virtual instrument or create new one
  Make sure Logical Name points to updated or new simulation virtual instrument
Notes: The final step in customizing the driver is to update the MAX configuration utility to point the Logical Name to the new driver. This involves the following steps:
You first create a new Simulation Driver that points to the new location of the DLL on your system.
You then need to update the existing simulation virtual instrument or create a new one that points to this newly created Simulation Driver.
Once that is done, modify your virtual instrument to use this new virtual instrument as its Simulation driver, and make sure the Logical Name still points to it.

## Slide 32: Fourth Demonstration
Fourth demonstration shows:
  How to customize class simulation driver user interface
  How to compile new class simulation driver DLL
  How to update configuration to use new driver
Notes: In this fourth demonstration, we show how a user can customize the class simulation driver user interface and behavior, how to compile the modified driver into a new DLL, and how to update the configuration file to use the new driver the user has created.

## Slide 33: Conclusions and Summary
Many benefits of simulation
  Test instrument functionality
  Simulate production hardware
Two levels of simulation
  Specific driver level – basic simulation
  Class driver level – advanced simulation
Non-interactive simulation
  Programmatically set simulation parameter values
  Simulation data from text file, database, and so on
Create custom simulation driver
IVI Simulation also works in LabVIEW 6i
Notes: This workshop has shown how you can take advantage of IVI simulation to simplify your test program development, by being able to test instrument functionality prior to purchase and being able to simulate your production floor hardware in your development lab. We saw that you can enable basic simulation at the specific driver level, and that more advanced simulation features can be obtained at the class driver level. You also saw the difference between interactive and non-interactive simulation, and how you can set the values of simulation parameters programmatically or through the Simulation Virtual Instrument’s Default Setup. You also learned how you can create a custom simulation driver to further enhance your ability to simulate your instrument and your actual data.
Finally, please note that although we have focused this workshop on how to use IVI simulation in Measurement Studio, the concepts and examples shown here can also be implemented and used in LabVIEW 6i.

## Slide 34: Questions and Comments
Thank you for attending
More Information @ ni.com/express
Express Code: niweekWS2E
Notes: Thank you for attending this workshop on using IVI drivers in Measurement Studio and on taking advantage of the many benefits of IVI simulation. We will now entertain any questions or comments that you may have.