## Slide 1: Building a Network-Based Data Logger
Tom Magruder
Product Manager
Fri Aug 18
10:15-11:30 a.m., 1:45-3:00 p.m.
Cypress (8B)
Notes: National Instruments data acquisition hardware and LabVIEW software provide the ideal platform for developing a network-based data logging system. In this session, you learn how to acquire data remotely, log data to disk, and share it throughout your network. Learn to build a network-based data logger by choosing the hardware platform that best suits your application.

## Slide 2: Overview
Background on network technologies
Three steps to building a network-based data logger
Conclusions/questions/more information

## Slide 3: What Is a Network-Based logger?
Acquire and log signals from data acquisition device, which may be local or distributed on the network
Data may be saved and displayed locally, or by another computer on the network
Acquisition can be low speed (temperature signals) or high speed (vibration monitoring)
Notes: Data logger – an instrument that logs and/or plots one or more channels of analog or digital data. Data logging are performed by dedicated instruments or by computer-based data acquisition (DAQ) systems.
Network-based data logger – a data logger that leverages internet technology to acquire, store, and publish data remotely. The network-based data logger makes the location of the data acquisition equipment, the PC, and the end-user, irrelevant.

## Slide 4: Network Technology – NI-DAQ
NI-DAQ turns a PC into a networked DAQ system
A PC treats networked DAQ device the same as local device
Two-step process to set up networked DAQ device

## Slide 5: Network Technology – NI-DAQ
Step 1: Launch remote device access (RDA) server on remote machine

## Slide 6: Network Technology – NI-DAQ
Step 2: Add RDA device in measurement & automation explorer (MAX) on local PC

## Slide 7: Network Technology – DataSocket
Read and write data between different data sources and targets
Specify data sources and targets through a URL scheme, just like you access Web pages in a Web browser
Built-in security to control data access.
Included with LabVIEW and Measurement Studio™

## Slide 8: Network Technology – DataSocket
LabVIEW 6i features provide DataSocket set-up from front panel menus.
Controls post data to network
Indicators read data from network
Adding DataSocket connection

## Slide 9: Building the Network-Based Logger
Acquire data locally or remotely
Store data to disk locally or remotely
Network connectivity depends on acquire and store choices

## Slide 10: Building the Logger – Acquisition
Use named channels
  Scales data to engineering units before saving.
Choose acquisition type based on data rate
  Easy I/O (software timed) when <500 Hz, timing not critical
  Buffered I/O (hardware timed) when >500 Hz or timing critical
Notes: With named channels (or virtual channels), you acquire data in engineering units such as degrees, psi, amps, and so on.
Choose the acquisition type based on the requirements of the logging tasks. For slow speed applications where the exact timing between samples is not critical (such as temperature monitoring), use the easy I/O VIs. For higher speed applications, or applications requiring exact timing of sample rate, use a double-buffered acquisition built with the intermediate I/O VIs.

## Slide 11: Building the Logger – Acquisition
Buffered (Timed) Acquisition
Easy I/O Acquisition

## Slide 12: Building the Logger – Storage
Choose file type based on requirements
  ASCII text file – for easy import into spreadsheets, but slow
  Binary file – fastest, but requires conversion before use in other applications
  Database file – can log to database files using SQL toolkit

## Slide 13: Building the Logger: Storage
Use file I/O VIs to log data to hard drive
Most efficient method
  Open file once (before starting acquisition)
  Write data inside of while loop
  Close file when done

## Slide 14: Building the Logger – Connectivity
Determine network connectivity by acquisition and storage requirements
Remote acquisition – use NI-DAQs RDA to acquire data from a remote PC
Remote storage – use DataSocket to publish data to network. On a remote PC, use DataSocket to subscribe to data, then save

## Slide 15: Use and Recommendations
Remote measurement – measurement node is next to a noisy machine, in a hazardous environment, or in an inaccessible location
Remote publishing and storage – data needs to be distributed to multiple users, or remote locations
Mix and match – any combination of remote measurement, publishing, and storage

## Slide 16: Hardware Selection
DAQ/SCXI Platforms
  PC
  PXI System
  Wireless
FieldPoint
Notes: PC – allows use of existing equipment. Good choice for low to medium channel count applications.
PXI™ – allows combining DAQ/SCXI/computer into single chassis. Rack mountable and rugged. Ideal for high channel count applications.
Wireless – Alliance Member (ViaSat) puts our DAQCards into a package with a wireless modem, allowing a wireless RDA device.
FieldPoint™ – low-cost, distributed I/O. Excellent choice for low-speed, widely distributed applications.

## Slide 17: Network-Based Data Logger Example
Monitoring performance of a turbine in a power plant
  Requires remote acquisition – DAQ system is next to a noisy turbine, engineer needs to log data from office
  Requires remote publishing – engineer needs to share data with headquarters in the next state
  May require remote data storage – headquarters may also want to log data for records
Notes: Show example of network-based data logger. Use RDA to acquire data from remote DAQ system. Log this data locally. Use DataSocket to publish this data to the network. With another VI on a different computer, use DataSocket to subscribe to this data, display it, and log it.

## Slide 18: What about Control?
What if you need user control through the network?
  Use DataSocket!
If time-critical control is required, use LabVIEW RT

## Slide 19: More Information
Visit the NI Developer Zone at zone.ni.com for more info
  Search under “RDA” for detailed information on Remote Device Access
  DataSocket information available
  Many example programs on data logging posted
Questions?