## Slide 1: Machine Monitoring and Control
John Hanks
Machine Vision Marketing Director
Fri Aug 18
10:15-11:30 a.m., 1:45-3:00 p.m.
Pecan (9B)

## Slide 2: Topics
Machine control applications and trends
NI technologies for machine control
Machine monitoring basics
NI technologies for machine monitoring
LabVIEW™ 6i features for machine control and monitoring
Notes: In this session, you learn about machine control trends such as enterprise connectivity and integrated hardware and software platforms. In addition, there is a basic introduction to machine monitoring. We also review new LabVIEW 6i features for machine control and monitoring.

## Slide 3: Machine Control Applications
Semiconductor tools
  Compound semiconductor manufacturing
    laser diodes, solar cells, LEDs
  Holographic and X-ray lithography
Material science
  Thin film microcoating
  Combination material science
  Glass and optical switch manufacturing
Manufacturing
  Smart card, plastics, disk drive sputtering, wave solder manufacturing, chocolate packaging, thermal forming, metal cutting
Laboratory
  Therapy guidance

## Slide 4
Ethernet
Subsystems
Real-time
controller
Ethernet
Industrial
network
I/O device
HMI
Enterprise
Ethernet
Motion
Vision
Monitoring
Typical Machine Architecture
Machine
Notes: Semiconductor machines often use both real-time and non real-time components. Users often use a combination of standard PC and industrial networks. More and more machines use networks so that automation engineers can monitor and trend conditions, predict failure, and prevent machine faults. Managers also use the network to review performance, improve efficiency and operation cost. The real-time components are typically single I/O points that control logic. The subsystems used for motion, vision, and monitoring are data intensive components requiring processing speed. Often these subsystems process data on standard PC platforms and return results to the real-time manager.

## Slide 5: Typical Industrial Machine Design Overview
Industrial
PC
Communications
DeviceNet
PROFIBUS-DP
Motion
material handling
Sensors
analog I/O
digital I/O
Vision
guidance
inspection
Material transport
conveyor
Component
Network
Notes: Machine developers choose to use industrial computer-based on PCI, PXI™/CompactPCI for ruggedness, small form factor, and availability of standard components and I/O devices. PXI offers the capabilities necessary for creating an integrated manufacturing machine. Many options are available for device communications, including DeviceNet, Ethernet, and PROFIBUS. National Instruments IMAQ™ and motion control products offer higher performance machine vision for online inspection, alignment, part guidance, assembly verification, counting, sorting, and bar code reading. National Instruments motion controllers feature onboard processors programmable through LabVIEW for reliable real-time motion control.

## Slide 6: Machine Trends
1. PC-based solutions
  Simplify development and maintenance with integrated software and hardware platform
  Low cost, flexible off-the-shelf solutions
  Extensions for real-time
2. Machine condition monitoring
  Minimize machine production downtime
  Machine protection
3. Enterprise connectivity
  Monitor/improve performance and efficiency
Notes: Because machine manufacturers demand quick time-to-market, easy machine modification, and lower overall component and development costs, the machine market is rapidly embracing open PC-based architectures such as PXI, LabVIEW, and Windows NT and plug-in boards for I/O, motion control, and vision. From machines that pleat coffee filters to machines that package chocolate candy to machines that make plastic sheets of credit cards, National Instruments PC-based measurement, vision, and motion control products simplify the entire control system lifecycle from development to startup and maintenance by providing an integrated software and hardware platform for measurement and control applications. National Instruments LabVIEW software integrates these components with the PXI/CompactPCI computer system providing industrial packaging, easy I/O connectivity, servo and stepper motor control, and image acquisition for digital and analog cameras.
Low cost networked PC-based measurement technology provides machine builders with the tools for machine condition monitoring to predict maintenance and prevent downtime, and to protect machines and products by shutting the machine down when a dangerous event occurs.
Because of the proliferation of the Internet and networks, automation engineers are taking advantage of these technologies for machine condition monitoring and distributed processing. NI products leverage readily available low cost network technologies such as Ethernet to provide networked measurements, vision, and motion control. Corporate managers are also using the network to review yield analysis, track production, and monitor yield.

## Slide 7: Trend 1 PC-Based Machine Control
PC-based
PLC and PC-based
PLC-based
PLC
Machine
Machine
Industrial PC
Network
Industrial PC
Network
Machine
PLC
Notes: Traditionally, PLCs control many machines. These are often stand-alone systems with little or no connectivity to the other control systems in the factory. Such systems often control the operation of the machine, but provide no data on machine operation. PLCs often rely on proprietary communications protocols and distributed processing and logic to coordinate I/O, motion, and vision. PLCs are reliable and have a huge install base. However, because PLC systems are based on programming languages that are not optimized for applications that require motion and vision, such as relay ladder logic, they can be difficult to program. In addition, ladder logic requires intensive knowledge of low-level bits and protocols, so they do not lend themselves easily to motion control and vision applications requiring complex mathematical algorithms. PLC systems are best suited for control applications with significant levels of discrete I/O. Although you can integrate motion, I/O, HMI, and vision components to a PLC-based system, you often need several different software tools.
Connecting the machine to industrial and corporate networks is critical to business success today. It is easy with platforms such as PCI or PXI because they can handle a wide range of industrial and enterprise communications protocols. Because LabVIEW and PXI use standards such as Window NT and CompactPCI, they offer flexibility and an open architecture for modifying and updating your machine as needed.

## Slide 8: Machines Builder Challenges
PLC
HMI
Motion
Vision
Ladder logic
Visual Basic
C
Proprietary
Monitoring –
data acquisition
LabVIEW
Notes: Machine builders often face the challenge of putting together components that have different software languages and hardware platforms. Is there a better way?

## Slide 9: One Software Platform Simplifies Development
HMI
Control logic
Motion controller
Networking
I/O and monitoring
Vision
Real-time
Drives and motors
Cameras
Industrial PC
Sensors
Notes: Today, the trend is for a more integrated hardware and software approach to machine control and monitoring. The PCI and PXI bus, because of their numerous I/O options, are commonly used in industrial applications. For example, the PXI hardware platform offers integration of motion control, image acquisition, analog and digital I/O, networking, and even instrumentation plug-in boards in one compact form factor. PXI also offers advanced performance with a built-in timing bus for synchronizing and triggering diverse I/O such as motion and vision. From a software perspective, using LabVIEW as your software development environment for control logic, data acquisition monitoring, operator interface, inspection, and communications can save you development time and money. The proven productivity, ease-of-development, and diverse I/O capabilities in LabVIEW allows you to develop machine control and monitoring applications with minimum effort and cost. PC-based machine control and monitoring has significant advantages whenever intensive communications or large amounts of data processing are required. The PCI and PXI bus are well suited for moving large blocks of data such as images and digitized analog signals for processing. In addition, by developing a software operator interface using a PC, you can design in advanced troubleshooting diagnostics to minimize operator set-up and machine down time.

## Slide 10: One Hardware Platform Simplifies Development
Industrial PC –
CompactPCI or PXI
Motion
Analog I/O
Vision
Digital I/O
Instruments
Networking
Control and HMI
software
Real-time
Notes: Because machine control and monitoring systems vary greatly in size, performance, and function, you need a solution that is both flexible and scalable. PXI answers these challenges with its modular architecture and standard software. With PXI, you use the same software you use with desktop PC systems, but in a more rugged package that includes plenty of expansion slots for your data acquisition, motion, and vision modules. Best of all, PXI leverages off of standard computer components, so you get these benefits at a a low cost.

## Slide 11: Example – Integrated Motion and Vision
Vision locates patterns fast
Resistant to changes in
  Lighting, rotation, focus, occlusion
Locate and move simultaneously with dual processor architecture
  Motion boards have onboard processor
IMAQ pattern matching
software
Notes: An example of integrated I/O is motion and vision. The technology that links vision to motion in PCB alignment and part placement applications is pattern matching. Pattern matching provides information about the presence or absence, number, and location of the model within an image. For example, you can search an image containing a printed circuit board for one or more alignment marks called fiducials. You can use the positions of the marks to align the board for chip placement from a chip-mounting device. In addition, you can use pattern matching to locate key components in gauging inspection applications. In gauging applications, the system locates key components. Then, the distance or angle between these objects is “gauged.” If the measurement falls within a tolerance range the part is good; if it falls outside the tolerance the part is rejected. In many applications, searching and finding a feature is the key processing task that determines the success of the application.

## Slide 12: MAX Benefits for PC-based Machine Control
Configure and set-up
  Analog I/O, digital I/O, motion, vision, and communications
Simplifies test and diagnostics
Speeds development with one API
Less driver conflicts
  Designed to work together
Vision
PXI/PCI Bus
Motion
DAQ
Com
MAX
Notes: With National Instruments hardware, such as data acquisition, image acquisition (IMAQ™), and motion control, you can use the Measurement & Automation Explorer (MAX) to quickly test connectivity, acquisition, and control. In addition, you can rapidly display signal, image, and data results. You can use MAX to configure the features of your boards in a consistent manner. For data acquisition this could mean setting the input for differential signals and for IMAQ this could mean setting the board for RS-170 camera input. The goal of MAX is to deliver a consistent interface for managing and configuring all of your measurement devices.
LabVIEW and our driver software give you a common software platform for numerous types of measurements. For example, the NI-DAQ™ and NI-IMAQ™ driver software application programming interfaces (API) are similar. If you know how to use our DAQ driver software, you can use this knowledge with product lines such as IMAQ, motion control, and GPIB. In addition, our driver software is scalable. The same function, IMAQ Snap, can acquire an image from a low-cost monochrome camera, a color camera, and a high-resolution digital camera. MAX simplifies configuration and test and reduces code rewrite when you want to move between hardware products in the same product line. In addition, your integrated measurement environment needs to have an open architecture. From LabVIEW you can call dynamic link libraries (DLLs) and interface ActiveX controls. Other programming benefits include logically named functions and consistent parameter names, attributes, examples, and error handling.

## Slide 13: LabVIEW RT Architecture
Host PC
Target RT engine
Download
application
Notes: WS3C-<number>
<footer>Machine Control and Monitoring
<header>
<date/time>
You can use LabVIEW RT for machine protection to monitor the state of a machine and then to shutdown the machine to prevent catastrophic damage to the machine, production line, part being manufactured, and workers. With LabVIEW RT, you develop in LabVIEW on a Windows computer, then download your real-time application to run embedded on an independent RT Series data acquisition board or PXI controller. These hardware targets run the user-developed code in the LabVIEW RT engine using a real-time operating system kernel.
Users have started using LabVIEW RT and RT Series hardware for machine monitoring and control applications. The rapid development environment, and reliable real-time performance of off-the-shelf hardware makes it an attractive alternative to custom designs that are more difficult to develop and hardware to maintain for the long term.

## Slide 14: Machine Monitoring System with RT
Win GUI
RT
DSA
DAQ
DAQ
Rotating machine
Vibration monitoring with DSA
Safety shutdown with dedicated real-time I/O
DAQ for temperature/strain/pressure
Notes: WS3C-<number>
<footer>Machine Control and Monitoring
<header>
<date/time>
One typical configuration of a machine monitoring system is a Windows computer with DAQ, dynamic signal acquisition, and RT all on a PCI backplane monitoring a rotating machine. The vibration, temperature, and strain are measured and displayed, while RT monitors some critical parameters and performs a real-time safety shutdown if necessary. As an example, National Instruments Alliance member Dateppli built a turbo charger test machine for IHI Turbo America. Each turbo rotated up to thousands of RPM, monitored by PCI data acquisition cards, while RT functioned as the emergency stop.
The plug-in PCI or PXI RT intelligent data acquisition card easily adds a real-time independent component to an existing Windows system.
The RT cards have analog I/O, digital I/O and counter timer I/O included, making them flexible enough to fit many applications. They communicate to the host PC through shared memory or TCP/IP.

## Slide 15: Machine Control System with RT
PID/fuzzy logic control algorithms and advanced analysis with LabVIEW
Real-time embedded control system
Remote access from Windows machine
Windows application
Machine
Ethernet, RS-232 (optional)
RT PXI embedded controller
Analog and
digital I/O
Notes: WS3C-<number>
<footer>Machine Control and Monitoring
<header>
<date/time>
Users may also need a complete real-time embedded system, with more I/O points and headless operation. The RT Series PXI/CompactPCI controller, with chassis and I/O acts as a customizable real-time box that can run any control or analysis developed by LabVIEW.
The PXI controller can run a real-time application at bootup and can communicate via TCP/IP to host computers, or just run standalone. It can also use the Ethernet, onboard GPIB, and Serial ports to connect to other subsystems.
The benefits of using LabVIEW and the real-time PXI controller for machine control development include the following.
  Instant, easy Internet connectivity for Web-enabled machines
  Powerful, flexible software development with built-in tools for PID and Fuzzy logic control, plus advanced analysis that can be downloaded with a mouse click to run real-time
  Off-the-shelf wide range of industry standard quality I/O hardware to insert in the platform

## Slide 16: Benefits of LabVIEW and PC-based Machine Control
Integrated software and hardware platform
Rapid development
Extensions for real-time performance
Seamless network connectivity
Ability to build advanced diagnostic and trouble shooting
Easy to maintain off-the shelf components
Notes: WS3C-<number>
<footer>Machine Control and Monitoring
<header>
<date/time>
With LabVIEW, you take advantage of the benefits of a rapid development environment and Windows connectivity. Plus, you can easily add the reliability of embedded real-time control.
You can build next generation machines with the ability to network to enterprise-wide systems. By using off-the-shelf PXI/CompactPCI, and PCI hardware, you create a system that is easy to maintain and scale for future needs.
LabVIEW and PC-based machine control systems reduce system downtime by providing detailed diagnostics. The LabVIEW flexible user interface can show the machine status on the PC screen and prompt your machine operator through repair steps. By building diagnostics into the LabVIEW application, machine operators can clear faults and repair equipment failure by following graphical directions displayed on the screen. Overall, this intelligent and fast troubleshooting dramatically reduces downtime.

## Slide 17: Trend 2 Machine Monitoring
Sensors and calibration
Conditioning
DAQ and DSA plug-in hardware
Motion boards with DAQ
DSA analysis software
Personal computer
Notes: Dynamic signal analysis (DSA) hardware provides many machine monitoring features. DSA hardware provides built-in antialias filtering and simultaneous sampling. Antialias filters prevent frequencies that are above the nyquist frequency from appearing as an “alias” in your frequency domain analysis. Use simultaneous sampling for machine condition analysis where phase measurements are important.
National Instruments motion boards include analog inputs so you can monitor the state of the machine and check out of bound conditions. Monitor the analog inputs for machine protection and store a signature analysis for monitoring and predict maintenance.

## Slide 18: Monitoring Definitions
Preventive maintenance – scheduled equipment service (lubrication, cleaning) prevents machine downtime
Predictive maintenance – monitor and detect machinery problems before they occur
Performance monitoring – monitor performance to improve machine operational efficiencies
Machine protection – shut down machinery to save product, machine, and production line
Notes: In this session, we focus on predictive maintenance and machine protection. New LabVIEW 6i measurements functions, such as limit testing, offer machine protection. Plus, many simple measurements can help you track the health of your machine and make your system more productive.

## Slide 19: Predictive Maintenance
Identifies failures before they occur
Schedule off-line repair to minimize downtime
Production benefits from higher productivity of equipment and personnel
Notes: Smart Signal (smartsignal.com) offers a product that uses historical trends for many measurements including temperature, vibration, and pressure to predict maintenance and failures. Smart Signal software is based on LabVIEW. Predictive maintenance rather than scheduled maintenance reduces cost by using less downtime and by not replacing good components.

## Slide 20: Sensors
Accelerometers
  Measure velocity and displacement
  1D to 3D (triaxial) accelerometers
ICP accelerometers
  Simple constant current conditioning (18-30VDC: 2ma)
  Fixed sensitivity, temperature range up to 350 °F
Charge mode accelerometers
  Variable sensitivity and temperature range up to 1000 °F

## Slide 21
Phase Analysis
Measure 1 and 2 simultaneously
The 1X vibration is 0º phase difference
Monitors load unbalance and shaft misalignment
Trend for predictive maintenance
Trigger shutdown when out of range
1
2
Notes: You can use phase analysis to determine if a rotating shaft is misaligned or the load is unbalanced. Data collected from two accelerometers analyzed in the time domain show if the two signals are in phase. In addition, you can measure phase with one tachometer and one accelerometer.
Set limits for phase for machine protection and trend phase over the lifetime of the machine for predictive maintenance.

## Slide 22: Orbit Analysis
Proximity probes
  Measures gap distance between probe and surface
  Measures continuous vibration of surface
Measure
  Shaft vibration
  Shaft orbital motion (radial position)
Machine protection and
  Shutdown when outside ranges
Trend for predictive maintenance
Shaft center line
X
Y
Y
X
Shaft radial position plot
Notes: Shaft position is a powerful machinery protection and management tool. Proximity transducers are two useful measurements. They provide a DC voltage that represents the gap distance between the probe tip and the shaft surface, and they provide continuous vibration measurement of the surface. With XY proximity transducers, you can measure shaft centerline position.
You can use specified gap limits, vibration limits, and radial limits to protect the machine. In addition, you can trend the measurement ranges for predictive maintenance.

## Slide 23: Order Analysis
Analysis technique rotating machines which operate over a wide range of speeds
Express the frequency content as a function of orders, (that is, harmonics of the rotational speed)
  For 3,000 rpm
    order 1 = 50 Hz, order 2 = 100 Hz, …
  For 6,000 rpm
    order 1 = 100 Hz, order 2 = 200 Hz, …
Notes: An order analysis example, a part of the key note presentation, is an area of research for National Instruments. Order analysis is a technique dedicated to the analysis of rotating machines operated in a wide range of speeds.
The purpose of order analysis is to express the frequency content at any rotational speed as a function of orders. Orders are basically harmonics of the rotational speed. But due to the various complex phenomena involved and, sometimes, multiple rotational speed of different parts, orders can be noninteger multiples of the fundamental frequency (first order).
A typical example could be a four-cylinder engine during a run-up test. The major source of noise and vibration from this engine is related to the combustion process, which happens twice per revolution, thus leading to a strong contribution of the second order. At 3,000 rpm, the second order corresponds to 100 Hz, but at 6,000 rpm it shows up at 200 Hz.

## Slide 24: Sampling for Order Analysis
Sampling synched rotation speed (Samples/revolution)
FFT used for order domain (amplitude/rev)
Constant samples/sec
Constant sample/revolution
Notes: Orders simplify machine analysis. The sampling rate is determined by the rotating speed of the device. Tachometers can supply a pulse train for triggering sampling. The fast Fourier transform (FFT) is used to transform the data into the frequency or order domain. The result is a graph that shows amplitude per revolution. The graph shows peaks that correspond to orders.

## Slide 25: Oil Whirl
Conditions
  light radial load
  excessive clearance between shaft and casing
Symptoms
  <0.5 order
Shaft
Oil
Amplitude
Orders
1x
0.40x
Notes: Misalignment of a shaft in a casing with lubricant can cause what is called oil whirl. For an ideal shaft located in the center, a 0.5x order is predicted. Imagine a thin film of the oil closest to the shaft moving at the same speed as the shaft. At the casing wall, a thin layer of oil is not moving at all or at zero velocity. So, the average velocity of the oil between the shaft and the casing is 0.5x, the shaft speed. If the shaft is not in the center of the casing, turbulance in the oil causes the oil to move at speeds below 0.5x orders.

## Slide 26: Misalignment
Often 2X order has greater amplitude
Angular misalignment causes axial vibration
180° phase change across coupling
Amplitude does not increase with speed
Coupling
Parallel
Angular
1x
2x
3x
Orders
Notes: When two vibration sources are at the same frequency, the spectra may contain sum and difference components causing orders at 2X, 3X and so on. For misalignment, the 2X amplitude can be greater than the 1X amplitude. If there is angular misalignment then there typically is axial vibration. A coupling causes 180º phase difference in vibration the axial direction. The amplitude does not increase with speed.

## Slide 27: Benefits of Order Analysis
Predictive maintenance of rotating machines
  Single rotation speed
  Many rotation speeds (ramp-up)
Defects at 1X operating speed (revolutions)
  Missing or cracked blades
  Load imbalance
Defects at 2X operating speed
  Misalignment of shaft
  Bent shaft
Notes: Rotating machinery defects often have specific vibration patterns or signatures. Spectrum analysis of running vibration gives important insights to defects within the machinery. A “golden master” template of a spectrum for a new deployed machine is useful in later analysis and diagnosis.
Missing or cracked blades cause an imbalance that is detected as a vibration at the operating speed. The same artifact often occurs with a rotating machine with a load imbalance. Envision gum stuck on a bicycle tire. On every rotation of the wheel, you can feel the imbalance. A high level of axial vibration and a large order at 2X the rotational speed often is a misalignment in the axial direction of the shaft of the rotating machine.

## Slide 28
Courtesy of Spectra Quest, Inc.
Machine Fault Analysis
and Order Tracking
Machinery fault simulator

## Slide 29: Machine Protection
Shuts down machinery to avoid catastrophic damages
For hazardous environment or costly machines
Analysis stops the machine

## Slide 30: New LabVIEW 6i Machine Protection Feature – Limit Mask
“Accept region” for time or frequency domain waveform
Characterize with high and low masks
Perform multiple limit mask
Use NI motion boards with analog inputs for machine monitoring
Notes: Limit testing is a method of monitoring the signature (general shape) of a waveform. This technique is used in the telecommunications industry to check for standards compliance and for machine condition monitoring to check for machine problems.
You can characterize the proper working state of a rotating machine by examining vibration or acoustic signals. You first characterize a machine by defining the high and/or low limits for the machine in several operating modes. For instance, you might choose operating modes such as normal, check (maintenance required), or failure. For each of these modes, you would gather (or estimate) the high and low limits.
These high and low limits define several regions of interest (mask) that you can then use for monitoring of a running machine.
You can also use National Instruments motion control boards for machine monitoring because they include analog inputs. Use these analog inputs to identify friction, inertia, overloading, and power dissipation for machine problems. An increase in temperature caused by friction build-up may mean the lubrication system is failing. Use stored signature analysis for monitoring to predict maintenance.

## Slide 31: Machine Monitoring Applications
Machine control and monitoring of magnetic bearings
Vibration predictive maintenance for aluminum extrusion machines
Monitoring hydro-electric machinery
Power grid monitoring and predictive maintenance
Refineries looking for less costly machine monitoring

## Slide 32: Trend 3 Enterprise Software for Machine Control and Monitoring
New LabVIEW 6i features
  Publish/subscribe
  Every control or indicator is DataSocket aware
  HTML reports generation tools
  LabVIEW Player™
  Create DLLs or shared libraries from VIs
Notes: You can right-click on any control or indicator and publish or subscribe to any data shared through DataSocket. This option is completely configuration-based and does not require diagram code.
You can now use the NI-Reports framework to create and publish HTML reports.
The LabVIEW Player is a version of LabVIEW designed to share your VIs through the Web. LabVIEW 6i users create VIs then distribute the applications to colleagues through the Web. Anyone not familiar with LabVIEW can download and install the Player from National Instruments. Once the LabVIEW player is installed, any VI you click on in a Web page automatically launches in the player. You can use the LabVIEW Professional Development System to create VIs that you can distribute to anyone with the player. The Player is free.
To connect to other development tools, you can turn your VIs into dynamic link libraries (DLLs) on the windows platform and shared libraries on the Mac, Linux, and Sun.

## Slide 33: LabVIEW for Machine HMI and Enterprise Connectivity
OLE for Process Control (OPC)
Alarms
Events
Historical data base
Servers for PLCs
Built in security (levels of access)
HMI wizard
Notes: There are many machine monitoring features that are a part of LabVIEW. OLE for process control (OPC) is an important feature to understand. It is an industrial automation standard for device and application software interoperability and distributed device control. Vendors provide OPC capabilities so that users can easily integrate their devices. More than 140 companies are a part of OPC.

## Slide 34: Summary
Machine builders use PC architectures
Big benefits
  Faster design cycles
  Faster machine evolution
  Low-cost monitoring
Machine monitoring saves money
Enterprise integration is key
Notes: WS3C-<number>
<footer>Machine Control and Monitoring
<header>
<date/time>
When you choose LabVIEW and the PXI or PCI as your machine control platform, you gain three main benefits – fast design cycles, less downtime through diagnostics, and the flexibility to evolve your machine.
With the graphical programming language of LabVIEW, you can significantly reduce machine control system design time. LabVIEW is an all-in-one, easy-to-use software tool that incorporates I/O, motion control, statistical process control (SPC), and machine vision, integrated with an intuitive operator interface. Bottom line, you can get your machine and production line up and running and get your product to market more quickly with LabVIEW.
Using a PC-based system, built on open industry standards, you benefit from an abundance of software and hardware I/O and you have the flexibility to quickly modify or update your machine control system to meet new customer or market demands. For example, with LabVIEW, you can add fuzzy logic control, Internet access for dynamic monitoring through the Web, structured query language (SQL) database capabilities, and high-speed data acquisition (DAQ) hardware for predictive maintenance.
With the flexibility and power of LabVIEW you can build low-cost machine monitoring, predictive maintenance, and machine protection into you new machines or add them to existing machines.