## Slide 1: Creating Measurement Studio™ User Interfaces
Denise Riedlinger
Software Engineer
Fri Aug 18
12:00-1:15 p.m., 3:30-4:45 p.m.
Cypress (8B)

## Slide 2: Agenda
LabWindows™/CVI
  Canvas control
  Table control
Visual Basic and Visual C++ tools
  2D Graphing
  3D Graphing

## Slide 3: Canvas Control
Text
Graphics
Images
Notes: The canvas control provides a high-performance, arbitrary drawing surface to LabWindows/CVI users. While it also is possible to draw into a graph control, the canvas control has the following advantages:
Speed – since the canvas control does not have to retain or map data, its performance exceeds that of the graph control
Pixel-based coordinates – coordinates in a canvas control are specified in pixels, instead of graph units. This makes it easier for the user to control where drawing occurs on the screen.
More drawing primitives – in addition to functions for lines, circles, polygons, bitmaps, and text, the canvas control includes functions which offer
Precise pen control – width, pattern, color, mode, and style
Clipping – setting and acquiring clipping rectangles
Inverting – color swapping, useful for highlighting, and so on
Scrolling

## Slide 4: Pen Configuration
Line styles
Line width
Fill patterns
Raster operations
Notes: ATTR_PEN_STYLE – a pen attribute that determines how lines and frames of geometric shapes are drawn. There are five different styles available, ranging from solid lines to dotted lines.
ATTR_PEN_WIDTH – a pen attribute that determines the thickness of lines, frames, and points.
ATTR_PEN_PATTERN – this attribute determines the pattern used to fill the interior areas of shapes. The value is an eight-byte unsigned character array representing a repeating eight-by-eight grid of pixels through which filling operations filter. A pixel of value 1 means that the pen fill color is used for that pixel. A pixel value of 0 means that black is used for that pixel.
Hint – to make a pixel value of 0 mean “screen color” instead of “black”, do this: First, set ATTR_PEN_PATTERN to the complement of the pattern you wish to use. Then, set ATTR_PEN_MODE to VAL_AND_MODE, set ATTR_PEN_FILL_COLOR to VAL_WHITE, and use a canvas draw function to fill the area. Then, set ATTR_PEN_PATTERN to the desired pattern, change the ATTR_PEN_MODE to VAL_OR_MODE, change the ATTR_PEN_FILL_COLOR to the desired pattern color, and draw again.
ATTR_PEN_MODE – determines the effect of drawing with the pen color (or pen fill color), given the current color on the screen. With the default setting, VAL_COPY_MODE, the current screen color is replaced by the pen color (or pen fill color). The other settings specify bitwise logical operations on pen color (or pen fill color) and the screen color.

## Slide 5: Transparency
Notes: By setting the background color (ATTR_PICT_BGCOLOR) of the canvas to VAL_TRANSPARENT, you can overlay the contents of the canvas onto other controls in your panel. This allows you to build complex images on a panel while incorporating the standard LabWindows/CVI controls in these images.

## Slide 6: More Advanced Features
Drawing options (ATTR_DRAW_POLICY)
  Update immediately
  Mark for update
  Direct to screen
Scrolling
  CanvasScroll (..., rect, dx, dy);
Clipping
  CanvasSetClipRect (..., rect);
Notes: Each canvas has an offscreen bitmap used to restore the appearance of the canvas when exposed. The ATTR_DRAW_POLICY attribute determines if and when drawing operations are rendered on the offscreen bitmap and the screen. There are three possible values –
VAL_UPDATE_IMMEDIATELY – drawing takes place offscreen. The bitmap section that corresponds to the area of the drawing operation is then copied into the canvas display.
VAL_MARK_FOR_UPDATE – drawing takes place offscreen. The area on the canvas that corresponds to the area of the drawing operation is marked for update instead of copied into the display. The new drawing becomes visible when drawing events are processed.
VAL_DIRECT_TO_SCREEN – drawing goes directly to the screen. The offscreen bitmap is not updated. Although this may result in a faster drawing time, whatever is drawn in this mode is lost when the canvas is redrawn.

## Slide 7: More Advanced Features (cont.)
Notes: The contents of a specific rectangular area of a canvas control are scrolled using the following function –
int status = CanvasScroll (int panelHandle, int controlID, Rect scrollRect, int scrollAmountInXDirection, int scrollAmountInYDirection);
The area exposed by the scrolling is filled using the current value of the ATTR_PEN_FILL_COLOR attribute. The contents of the canvas outside the rectangular area are not affected.
Drawing to a canvas control can be constrained to a specified clipping area, which can be set using the following function –
int status = CanvasSetClipRect (int panelHandle, int controlID, Rect clipRect);
Canvas drawing operations do not extend beyond the clipping rectangle. Any drawing outside the clipping rectangle has no effect, with the exception of CanvasClear, which is not limited by the clipping rectangle. Changing the clipping rectangle does not affect the current contents of the canvas.

## Slide 8: More Advanced Features (Cont.)
Batch drawing
  depth = CanvasStartBatchDraw (...);
  depth = CanvasEndBatchDraw (...);
Pixel values querying
  CanvasGetPixels (..., rect, pixels);
Notes: The drawing performance of the canvas control increases by surrounding drawing code with calls to the following pair of functions –
int nestingDepth = CanvasStartBatchDraw (int panelHandle, int controlID);
int nestingDepth = CanvasEndBatchDraw (int panelHandle, int controlID);
In general, use CanvasStartBatchDraw when you make two or more consecutive calls to canvas drawing functions. Match each call to CanvasStartBatchDraw with a call to CanvasEndBatchDraw.
Before LabWindows/CVI performs drawing operations, it invokes certain operating system functions to prepare for drawing on the particular canvas. Without batch drawing, LabWindows/CVI must call these system functions for each canvas drawing operation. With batch drawing, LabWindows/CVI calls the system functions only once for all of the drawing operations between CanvasStartBatchDraw and the matching CanvasEndBatchDraw.
The following code shows an example of how to incorporate a sequence of drawing operations on the same canvas control into one batch –
CanvasStartBatchDraw (panelHandle, controlID);
CanvasDrawLine (panelHandle, controlID, point1, point2);
CanvasDrawLine (panelHandle, controlID, point3, point4);
CanvasDrawRect (panelHandle, controlID, rect5);
CanvasEndBatchDraw (panelHandle, controlID);

## Slide 9: More Advanced Features (Cont.)
Notes: During a batch draw, you can call drawing operations on other canvas controls or call other User Interface Library functions that perform drawing operations or process events. This has the effect of implicitly ending the batch. The next time you call a drawing function on the same canvas, the batch is implicitly restarted.
You can nest calls to CanvasStartBatchDraw.
Failure to properly match CanvasStartBatchDraw and CanvasEndBatchDraw calls can negate the potential performance improvements but does not cause any other ill effects.
Do not access a canvas control from other threads while batch drawing is in effect for the control.
If the ATTR_DRAW_POLICY attribute for the canvas control is VAL_UPDATE_IMMEDIATELY, no update to the screen occurs until you end the batch. Also, changing values of the ATTR_DRAW_POLICY and ATTR_OVERLAP_POLICY attributes during a batch draw has no effect until after you end the batch.
The colors of the pixels in a specific rectangular area of a canvas control can be obtained using the following function –
int status = CanvasGetPixels (int panelHandle, int controlID, Rect rect, int pixelColors[]);
The canvas control maintains an internal bitmap reflecting all of the drawing operations (except for drawing operations made while the ATTR_DRAW_POLICY attribute is VAL_DIRECT_TO_SCREEN). Sometimes the internal bitmap contains the result of recent drawing operations not reflected on the screen. CanvasGetPixels obtains the pixel colors from the internal bitmap, not from the screen.

## Slide 10: Table Control
Numerics
Strings
Images
Notes: The table control provides a general-purpose device for storing and manipulating grid- , column- or row-based numeric, text, or image data.
A brief description of its programmatic interface follows.
Creating and deleting cells –
You can create an arbitrary number of rows and columns on a table control. As you do, you create table cells that store the data of the table control. The number of cells in a table always equals the number of rows multiplied by the number of columns. Also, the number of cells in a row is equal to the number of columns in the table, and vice versa.
You use the following functions to control the number of rows in a table control – InsertTableRows, DeleteTableRows, and GetNumTableRows. Analogous functions control the number of columns.
Cell Selection –
If you want to set the active cell programmatically, use SetActiveTableCell, or SetTableSelection if you wish to select a range of cells. SetTableSelection makes the top-left cell in the selection the active cell.

## Slide 11: Table Control (continued)
Notes: Cell Values –
Each cell has a type associated with it which determines what type of data you can store in each cell – numeric, text, or bitmap image. By changing the cell type, you can store all three types of values simultaneously in each cell, but only the value corresponding to the current cell type is visible and operable.
You can set and get the value of a cell directly, or you can set and get the values of a range of cells, such as those of an entire row, or a group of rows. You set the values of a range of cells in one of the following ways.
To set the values from an array containing the new value of each cell, use SetTableCellRangeVals.
To set the values from a single value which you want to propagate through each cell in a range, use FillTableCellRange.
To get the values from a range of cells, use GetTableCellRangeVals.
To set and get the values of a range of cells, all cells in the range that you specify must have the same cell type. Also, if the type is VAL_CELL_NUMERIC, the cells in the range you specify must also have the same data type.
To set and get the value of a single cell, use SetTableCellVal and GetTableCellVal.

## Slide 12: Table Control (continued)
Notes: Cell, Row and Column Attributes –
You can set attributes for each individual cell, using SetTableCellAttribute, and SetTableCellRangeAttribute. Cell attributes can be specific to a given cell type – essentially any attribute that you can set on a numeric control, a text box control, or a picture control, you can also set on a table cell – or they can apply regardless of cell type. Typical examples of cell attributes that you can set are, visibility of the horizontal gridline, background color of the cell, and floating point precision.
In addition to cell attributes, you can also set row and column attributes, using SetTableRowAttribute and SetTableColumnAttribute. Examples of row and column attributes are the column width and whether to replace numeric row labels with custom strings.
Searching and Sorting –
If you want to locate a particular cell value anywhere in the table, use GetTableCellFromValue. GetTableRowFromLabel and GetTableColumnFromLabel perform similar functions on row and column labels.
SortTableCells sorts a range of cells using the data in one of the rows or columns as the sort key. You can pass it a callback function which LabWindows/CVI calls whenever it needs to compare the values of any two cells, thus allowing you to customize the sort.

## Slide 13: Table Control (continued)
Notes: Copying and Pasting –
You can copy one or more cells to the clipboard using ClipboardPutTableVals. When the data appears in the system clipboard the <Tab> ASCII character separates the data of each cell, and the linefeed ASCII character <LF> separates the data of each row.
LabWindows/CVI skips picture cells when it copies cells to the clipboard, with the following exception – if you pass a range consisting of a single cell to ClipboardPutTableVals, and it is a picture cell, then the image contents of the cell are placed in the system clipboard as a bitmap image.
You can paste the contents of the system clipboard into a table control using ClipboardGetTableVals. LabWindows/CVI assumes that the <Tab> ASCII character separates the data that corresponds to each cell, and that the linefeed <LF> ASCII character separates the data corresponding to each row.
When the data in the clipboard includes an empty cell or cells, the paste operation makes no change to the corresponding cell or cells in the table that receives the new data. Similarly, when the data in the clipboard includes cells that contain data that cannot convert to a valid number, the paste operation makes no change to the corresponding cell or cells in the table that receives the new data.
If there is a bitmap image in the system clipboard and you wish to paste it into a picture cell, pass a cell range containing only that cell to ClipboardPutTableVals.

## Slide 14: Table Control (continued)
Notes: Pop-Up Menu –
To customize the table control pop-up menu, insert menu items corresponding to tools you would like to make available to the operator of the table. You specify a callback function and an item label, using NewCtrlMenuItem. Whenever the menu item is selected, LabWindows/CVI calls the corresponding callback function.
In addition to inserting your own menu items, you can remove the built-in items, included by default (Goto, Find, and Sort). Use HideBuiltInCtrlMenuItem and ShowBuiltInCtrlMenuItem to control the visibility of these items.

## Slide 15: Cell Attribute Inheritance
Notes: When you insert new rows and columns in the table, the new cells are created with an initial set of attributes. Depending on how you are using the table, you might want the initial state of new cells to match the state of its neighboring cells in the same column, its neighboring cells in the same row, or neither. The table attribute ATTR_TABLE_MODE determines how new cells inherit their initial, default set of attributes – from their parent row, their parent column, or the table itself.

## Slide 16: Row Mode
Configure master cell using SetTableRowAttribute
Notes: Any attribute which you can set via SetTableCellAttribute or via SetTableCellRangeAttribute you can also set as a row attribute, using SetTableRowAttribute.
When you set a cell attribute on a row, and the table mode is set to VAL_ROW, the row preserves this attribute value as a “master” to use as the initial value of the corresponding attribute on any new cells you create for that row.

## Slide 17: Column Mode
Configure master cell using SetTableColumnAttribute
Notes: Any attribute which you can set via SetTableCellAttribute or via SetTableCellRangeAttribute you can also set as a column attribute, using SetTableColumnAttribute.
When you set a cell attribute on a column, and the table mode is set to VAL_COLUMN, the column preserves this attribute value as a “master” to use as the initial value of the corresponding attribute on any new cells you create for that column.

## Slide 18: Grid Mode
Configure master cell using SetCtrlAttribute
Notes: Any attribute which you can set via SetTableCellAttribute or via SetTableCellRangeAttribute you can also set as a table attribute, using SetCtrlAttribute.
When you set a cell attribute on the table, and the table mode is set to VAL_GRID, the table preserves this attribute value as a “master” to use as the initial value of the corresponding attribute on any new cells you create on the table.

## Slide 19: Sorting
Programmatic sorting – SortTableCells()
  Custom sorting – CellCompareCallbackPtr
Interactive sorting
Notes: SortTableCells sorts a range of cells using the data in one of the rows or columns as the sort key. You can pass it a callback function which LabWindows/CVI calls whenever it needs to compare the values of any two cells, thus allowing you to customize the sort.
If you click on the right mouse button anywhere over the table control you activate a menu which contains predefined items, as well as items which you can include yourself.
The following tools correspond to the pre-defined pop-up menu items.
Goto – You specify a target cell to go to, using its row and column indices.
Find – You search all numeric and text cells in the entire table, or in a selection range, for a text string. After the initial search, you can press <F3> to find the next occurrence of the same text string, or you can press <Shift-F3> to search backwards for the next occurrence of the text string.
Sort – If a range of cells is selected, you can sort the cells in the range using the data in one of the rows or columns as the sort key

## Slide 20: Advanced 2D Graphing
Microsoft Visual Basic and
Visual C++ Tools

## Slide 21: User Interface Bindings
Utilize DataSocket technology
Connect properties on user interface controls to remote data sources and targets
Simplify the creation of remote monitoring applications

## Slide 22: Binding to a Sine Wave
Notes: Create a new binding and assign it a unique name
Browse the list of bindable properties and select the appropriate item
If you want to plot data from a data source, use the YData, XYData, YDataAppend, or XYDataAppend property. Setting the YData and XYData properties are equivalent to calling the PlotY and PlotXY methods, and setting the YDataAppend and XYDataAppend properties are equivalent to calling the ChartY and ChartXY methods.
Specify the URL, or browse for a data source by clicking the browse (…) button

## Slide 23: Binding to a Square Wave
Notes: Bindings update when the data value changes. For a square wave, the data alternates between two data values (0 and 5). If this data is bound to the Graph in ReadAutoUpdate mode, the waveform will appear to be a triangle wave.
To bind to a square wave, set the access mode to Read and specify a periodic interval to read and chart the data.

## Slide 24: Processing Data
Enable the DataUpdated event
Add data processing steps to the CWBindingDataUpdated event
  Index – which binding is being updated
  Data – the new data value
    Can modify in this event
  Ignore – return flag
    Set this to True and the bound property will not be updated
Notes: ‘Visual Basic code for processing data
‘Enable the DataUpdated event
CWGraph1.DataUpdatedEnabled = True
‘Add data processing in the Event handler
Private Sub CWGraph1_CWBindingDataUpdated(ByVal Index As Integer, ByVal Data As CWUIControlsLib.CWData, Ignore As Boolean)
Select Case CWGraph1.CWBindings(Index).Name
Case "RelayState"
'Turn the button on when the RelayState is high (>5)
CWButton1.Value = (Data >= 5)
Case "NoisySine"
'Simulate noise in the sine wave when the noise filter is off
If (NoiseFilter = False) Then Data = Data + Rnd
End Select
'Ignore negative values
If (Data.Value < 0) Then
Ignore = True
End If
End Sub

## Slide 25: Managing Multiple Plots
Plot template is the basis for all plots that are added in the property pages or using the Plots.Add method
MultiPlots are updated when an array of data is passed to the CWGraph plot or chart methods
TempPlots are automatically discarded when they are no longer needed
Notes: You can easily create several plots by passing a two-dimensional array to the PlotY or ChartY method. Each row contains data for a single plot on the graph. The graph, which contains a CWPlots collection that manages individual CWPlot objects, assigns each data plot to a CWPlot object. By default, the CWPlots collection contains one CWPlot object. If you pass data for only one plot, the graph uses the existing CWPlot object. If you pass data for four plots and you do not explicitly add more CWPlot objects, the graph automatically creates three more CWPlot objects to hold the remaining data.
Each CWPlot object created is based on the properties (line style, color, etc) specified in the PlotTemplate. Each CWPlot automatically created is a temporary multiplot.
The MultiPlot property determines if you can use the plot by the CWGraph plot or chart methods. If you pass an array of data to the CWGraph object, but you do not want to update the data in Plot2, set MultiPlot to false for that plot. To update the plot, call the plot and chart methods on the desired plot:
CWGraph1.Plots(2).ChartY Data
The TempPlot property specifies whether a plot can be discarded if the next CWGraph plot or chart method does not need it. Plots allocated at design time or by using the CWPlots.Add method have this property set to False. Plots allocated by a CWGraph plot or chart method have this property set to True.
When you call a Chart or Plot method on the CWGraph object and there are existing plots, the graph updates the data for each CWPlot object that has the MultiPlot property set to True. If there are not enough plots to hold all the data, temporary multiplots are created. If there are extra plots, the remaining CWPlot objects that are temporary plots will be discarded.

## Slide 26: Maximize Graph Performance
Select a line width of 0 or 1 for each plot
Set ImmediateUpdates property to False
Update the entire data set at once by using Multiplots when appropriate
Notes: Changing some properties of the ComponentWorks™ Graph control may increase drawing time and CPU usage. Drawing is a CPU intensive operation, and relies a great deal on the operating system. The following tips may help you maximize graph performance.
Thin Lines – Windows takes about twice as long to draw lines of width two. Lines of width three are even greater. Use lines of widthzero or one for fastest drawing.
Invalidation versus Immediate update – Immediate update mode will repaint the graph after any change is made. If you are making several changes, (such as individually updating separate plots) the invalidation mode is much better. When ImmediateUpdates is False, the container repaints the control when it has been invalidated. This similar to what ATTR_REFRESH_GRAPH is used for in LabWindows/CVI.
Multiplots – calling PlotY for each individual plot on the graph increases overhead. If you are updating multiple plots it is better to pass in the data as a 2d array with multiple channels with the CWGraph.PlotY method. If this is not reasonable, make sure ImmediateUpdates is set to false.

## Slide 27: Advanced 3D Graphing
Microsoft Visual Basic and
Visual C++ Tools

## Slide 28: Customizing the Color Map
Notes: Create a custom color spectrum for 3D data using the Color Map Browser. From the 3DGraph Plots Style property page, you can edit the Color Map.
To add a new element to the color map, select Add, then drag and drop the new item. The selected item is displayed with a black arrow next to it. Change the color or value for the selected item. Use the palette to select a basic color or pick a custom color from the color spectrum.
When the Autoscale property is true the color map stretches or shrinks itself so that the bottom of the color map maps to the minimum data value and the top of the color map maps to the maximum data value. Predefined color maps always auto scale regardless of the value of this property.

## Slide 29: Intensity Graph

## Slide 30: Intensity Graph
Customize the 3D Graph to create an Intensity graph
Set the view mode to the XY plane
Set the view distance so the plot will fill the plot area
Notes: ‘Visual Basic code for an Intensity Graph
CWGraph3D1.ViewMode = cwViewXYPlane
CWGraph3D1.ViewAutoDistance = False
‘View distance is defined in terms of a bounding box that surrounds the data
‘For a view distance of 1.0, the actual plot takes up only half of the plot area.
‘To fill the plot area, set the view distance to 0.5
CWGraph3D1.ViewDistance = 0.5

## Slide 31: Contours
Highlight X, Y, Z, or Magnitude data
Arrange contours at periodic intervals or specific levels
Anchor contours at a known level
Programmatically configure the level, line color, line style for each contour or for the whole collection
Notes: ‘Visual Basic Code fragments for programmatically changing all contours in the Contours collection
' Set the number of contours
CWGraph3D1.Plots(1).Contours.Levels = Levels
' Set the contour interval
CWGraph3D1.Plots(1).Contours.Interval = Interval
' Set the AnchorEnabled property
CWGraph3D1.Plots(1).Contours.AnchorEnabled = AnchorEnabled.Value
' Set the Anchor value
CWGraph3D1.Plots(1).Contours.Anchor = Anchor
' Change the line color for all contours
CWGraph3D1.Plots.Item(1).Contours.SetLineColor vbRed
' Change the line style for all contours
CWGraph3D1.Plots.Item(1).Contours.SetLineStyle cwLine3DSolid

## Slide 32: Interval Contours
Notes: Set the contour mode to Interval and specify the interval for regularly repeating contours.

## Slide 33: Level List Contours
Notes: For custom contours at specific levels, create a Contour Level List. Set the contour mode to Level List, and enter the specific values at which the contours will be drawn. This contour mode is useful for highlighting specific areas of the data, and easily determining which data points are at the same magnitude. In the screen shot above, the contours are specified in a level list so that contours are drawn only around the extremes – the highest and lowest points.

## Slide 34: Triangulation
Create a surface mesh of irregularly ordered data
Raw data displayed as points
Data triangulated into a mesh
Notes: The 3D Graph has a new method, Plot3D Mesh, which triangulates the data into a surface mesh.
CWGraph3D1.Plots(1).ColorMapStyle = cwColorSpectrum
CWGraph3D1.Plots(1).LineWidth = 0
‘To display the raw data, set the plot style to Point
CWGraph3D1.Plots(1).Style = cwPoint
‘To display the triangulated data, set the plot style to Surface + Line
CWGraph3D1.Plots(1).Style = cwSurfaceLine
‘To plot the x, y, and z vectors, use the Plot3DMesh method
CWGraph3D1.Plot3DMesh x, y, z