## Slide 1
Remotely Controlling Instruments over Ethernet
Brian Neidig
Senior Software Engineer
Chris Rake
Hardware Engineer
Fri Aug 18
12:00-1:15 p.m., 3:30-4:45 p.m.
Pecan (9B)

## Slide 2: Agenda
Introduction
Network basics
Ethernet basics
Network design factors
NI and Ethernet instrument control options
Case studies
Demonstration
Summary

## Slide 3: Introduction – The Problem
Need remote instrument control
  Cable limitations
  Remote monitoring
  Hazardous environments
Have limitations on system resources
  IRQs
  Card slots
Need sharing of instruments by multiple users
Notes: Ethernet has become a necessary component in today's business environment. However, Ethernet-based test and measurement applications are still in their infancy. The ability to connect all the components of your instrumentation system into one central networked application brings endless possibilities to engineers looking for better and more efficient ways to develop and test products. Traditionally, networked applications have been useful for overcoming physical limitations such as hazardous environments, cabling setup restrictions, or simply the control of systems in different locations. Many engineers are realizing that there is a bigger value on networked instrumentation systems than to overcome these physical limitations, the value of an easier and more efficient integration.

## Slide 4: Introduction – The Solution
Use existing infrastructure
  Ethernet network already exists in many areas
  Exploit the Internet
  Expanding the network is inexpensive
Incorporate traditional instruments
  GPIB
  RS-232/485
Networked Instrument Control
Notes: With Ethernet networking, you can create one system in which all the pieces are easily integrated together – you control instruments, acquire data, process it, send it to databases, analyze it, and present it efficiently by having immediate access to it from virtually anywhere. One of the main advantages of Ethernet is its widespread use. This allows you to take advantage of existing infrastructure (many companies already have this type of network installed), and the existing Ethernet domain knowledge within your organization.
Several instrument manufacturers have started manufacturing Ethernet-based instruments that can be connected to a network and accessed and controlled from any computer in the network. However, only a minimal number of Ethernet-based instruments currently exist on the market. Also, you may already have extensive test and measurement systems consisting of numerous instruments. To add Ethernet-based instrumentation to such existing systems, you do not need to replace all of your devices. With the National Instruments Ethernet-to-GPIB and Ethernet-to-Serial controllers, you can control your existing GPIB or serial equipment located anywhere in the world from your own desk via a standard Ethernet connection.

## Slide 5: Networking Basics Layers
Physical
Data link
Network
Transport
Transmits data over the medium
(fiber, twisted pair, RF, etc.)
Adds error detection, flow control, and
physical addressing
Adds addressing for switching and routing
Splits data into packets, and manages the
connection
Has data to send to another network node
(LabVIEW™, Netscape, FTP, Telnet, etc.)
Application
Notes: The Network stack consists of multiple layers of communication between network partners. The stack can be represented as several different models including the ISO OSI model (7 layers) and the Internet model (4 layers). For the purpose of this presentation, a 5 layer model is used:
Physical Layer – covers the physical interface between a data transmission device and a transmission medium and the rules by which bits are passed from one to the other. It is a raw bit stream service.
Data Link Layer – attempts to make the physical link reliable and provides the means to activate, maintain, and deactivate the link. The main service to higher layers is that of error detection and control; allowing the next higher layer to assume error-free transmission over the link.
Network Layer – provides for the transfer of information between computers across a communication network. It is responsible for establishing, maintaining, and terminating connections across the network. It relieves higher layers of the need to know anything about the underlying data transmission and switching technologies used to connect systems.
Transport Layer – provides a reliable mechanism for the exchange of data between computers. It ensures that data are delivered error-free, in sequence, with no losses or duplications. It may also be concerned with optimizing the use of network services and providing a requested quality of service.
Application Layer – provides means for application programs to access the network environment. This layer contains management functions and generally useful mechanisms to support distributed applications. In addition, general purpose applications such as file transfer, electronic mail, and terminal access to remote computers are considered to reside at this layer.

## Slide 6: Networking Basics Packet Creation
Physical
Data link
Network
Transport
Application
Data
Data 1 of 3
Data 2 of 3
Data 3 of 3
Data 1 of 3
Data 2 of 3
Data 3 of 3
Data 1 of 3
Data 2 of 3
Data 3 of 3
1011001....0110101
1011001....0110101
1011001....0110101
Network node 1
Notes: Each level of the network structure adds a header and possibly a trailer with the correspondent specific information to the package that needs to be transmitted. For example, after the application has been written and the Transport layer separates the information to be transmitted into packets, the Network layer adds the necessary addressing information to allow the packet to reach the destination even if it has to go through bridges or routers. This information is added as a header to the packet. In a TCP/IP network protocol, there is no trailer added at the network layer. Then, the data link layer treats the whole unit as data and appends its own header and trailer. The frame is now transmitted by the physical layer onto the transmission medium. When the frame is received by the target device, the reverse process occurs. As we ascend layers, each layer strips off the outermost header and trailer, acts on the protocol information contained therein, and passes the remainder up to the next layer.

## Slide 7: Networking Basics Packet Creation
Physical
Data link
Network
Transport
Application
Network node 1
TCP
IP
Ethernet
Physical
Data link
Network
Transport
Application
Network node 2
TCP
IP
Ethernet

## Slide 8: Ethernet Basics IEEE802.3 CSMA/CD
CSMA/CD
  Carrier Sense Multiple Access with Collision Detect
General transmission rules
Elements
  Physical medium
  Infrastructure
Notes: Many people use the word Ethernet to mean the entire communication process, when, in fact, it only defines the physical communication method.
Ethernet access is done using a method called CSMA/CD – Carrier Sense Multiple Access with Collision Detection. In this method, multiple interfaces or nodes can listen until no signals are present. If they think that no other interface is transmitting, they begin transmitting. If some other device is transmitting, there will be a signal on the channel, which is called carrier. All other interfaces must wait until the carrier ceases before trying to transmit, and this process is called Carrier Sense.
Multiple Access refers to the ability of every interface to send frames onto the network. No one gets a higher priority than anyone else. In addition, since signals get a finite time to travel from one end of an Ethernet system to the other, the first bits of a transmitted frame do not reach all parts of the network simultaneously. Therefore, it is possible for two interfaces to sense that the network is idle and to start transmitting their frames simultaneously. When this happens, the Ethernet system has a way to sense the “collision” of signals and to stop the transmission and resend the frames. This is called Collision Detect.
With this method, every interface has a fair access to the network. After the transmission of every packet is successful, all interfaces use the CSMA/CD protocol to determine which interface gets to use the Ethernet channel next.

## Slide 9: Ethernet Basics Physical Medium – Bus Topology
Terminator
GPIB
Terminator
GPIB
GPIB
10Base2 (Coax)
Up to 30 devices/segment
Segment length < 185m
Physical
Data Link
Network
Transport
Application
Notes: The physical medium (network cable) is very related to the topology type.
The above slide describes one case:
Bus – The Bus topology is the simplest. All interfaces are connected in succession on a single cable. All transmissions go to all the connected interfaces with each interface selecting those transmissions it should receive. Most Coaxial mediums are configured in bus topology. You can have up to 30 devices on each segment and the length of the segment should be shorter than 185 m.

## Slide 10: Ethernet Basics Physical Medium – Star Topology
Twisted pair (10/100BaseT)
Fiber optic (100BaseFx)
One device per segment
Segment length < 2,000 m (fiber), 100 m (twisted pair)
Physical
Data Link
Network
Transport
Application
PXI Real-Time
GPIB
Serial
GPIB
Repeater
Notes: The above slide describes another case:
Star – In this topology, all attached interfaces are directly wired to a central hub. This hub established, maintains, and breaks connections when an error occurs. Several different media use the star topology: twisted pair 10BaseT and 100BaseTX, and fiber optic100BaseFX. By having one interface per segment, each segment could be as long as <100 m.
Hybrid topologies that combine different types of media in a network system are not only possible, but common. There are many devices available that either convert one medium to another or work with multiple media types.

## Slide 11: Ethernet Basics Network Infrastructure
Hubs/repeaters
  Detects collisions
  Repeats all packets to all ports
Bridges/switches
  Detects collisions
  Forwards packets only to select ports
Routers/gateways
  Routes packets based on IP address
  Connects different network types together
  Connects different subnets together
  Backbones of the Internet
Physical
Data Link
Network
Transport
Application
Notes: To increase determinism, make the network easier to manage, and to increase the number of available valid addresses, a company utilizes three common components, including hubs/repeaters, bridges/switches, and routers/gateways.

## Slide 12: Ethernet Basics Network Infrastructure
Router
Router
Router
Router
Router
Router
Router
Bridge
Router
Router
Internet
Router
Workstation
Remote
Station
Hub

## Slide 13: Network Design Factors
1. Topology
2. Configuration
3. Throughput
4. Determinism
5. Instrument sharing
6. Security
Notes: There are several factors that you must consider when implementing a networked instrumentation system. We have listed what we consider the main factors. We will start with the topology of the system (or the network layout) and will explain the other factors later.
1. Topology
2. Configuration
3. Throughput
4. Determinism
5. Instrument Sharing
6. Security

## Slide 14: Network Design Factors 1. Topology – Network Layout
Network infrastructure
  If possible, use existing network
  Leverage company domain knowledge
Instrument types
  Traditional buses (GPIB, Serial)
  Ethernet-equipped instruments
Instrument location
  Local
  Remote
Instrument sharing
Physical
Data Link
Network
Transport
Application
Notes: There are several factors to consider before designing the network layout of your organization or your system. The first is to determine what type of network infrastructure, if any, you have already available. To find this information, consult with the network administrator. Leveraging their knowledge on Ethernet networks is another advantage of implementing such a widely used technology.
There are other factors that influence the way you lay out your networked system, such as the different instrument types, their location, and the need to share them among different users.

## Slide 15: Network Design Factors 1. Topology – Network Layout
Local
Remote
Physical
Data Link
Network
Transport
Application

## Slide 16: Network Design Factors 2. Configuration
Ethernet Address – 9A:7B:FF:16:D3:91
  Used by the Data Link layer for routing packets locally
  Globally unique – permanently assigned by the manufacturer
IP Address – 192.164.41.169
  Used by the Network layer for routing packets between networks
  Not unique – statically or dynamically assigned by network administrator
Subnet Mask – 255.255.255.0
  Used to determine the location of a destination of packet
  Network specific – assigned by network administrator
Physical
Data Link
Network
Transport
Application
Notes: Ethernet address: Globally unique address assigned by the manufacturer of the device. This is a permanent address and it is different from the IP address.
IP address: Computer-readable address of a device on your network. It can be assigned automatically or manually.
Subnet mask: A code that helps the network device determine whether another device is on the same or different network.
Subnet: A portion of the network, which shares a network address with other portions of the network and is distinguished by a subnet number.
Example #1
  192.164.41.169 with mask 255.255.255.0
  192.164.41 is the network ID
  41 is the subnet address
  169 is the device address
Example #2
  199.77.147.62 with mask 255.255.0.0
  199.77 is the network ID
  77 is the subnet address
  147.62 is the device address

## Slide 17: Network Design Factors 2. Configuration
Physical
Data Link
Network
Transport
Application
Local
Remote
Subnet mask = 255.255.255.0
192.164.41.1
192.164.41.2
192.164.41.4
192.164.41.3
192.164.42.1
192.164.42.2
Notes: Every device in the network needs an IP address. Some devices are able to obtain that address automatically, and others require a static IP address assigned to them. If you need to assign a static IP address and your network is administered by a network administrator, ask the administrator to assign an IP address and the other network parameters to your devices.
If you are assembling your own Ethernet network for your instrumentation system, you can choose your own IP addresses. The format of the IP address is determined by the subnet mask. If your subnet mask is 255.255.255.0, the first three numbers in every IP address on the network must be the same. If your subnet mask is 255.255.0.0, only the first two numbers in the IP address on the network must match. For either subnet mask, numbers between 1 and 254 are valid choices for the last number in the IP address. Numbers between 0 and 255 are valid for the third number of the IP address.
Note that you can create networked systems that contain instruments in different subnets. In the illustration above, each building has its own subnet. However, the computers in subnet 20 are able to control the instruments in subnet 21.

## Slide 18: Network Design Factors 3. Throughput
Network capacity
  10 and 100 Mbits/s, 1,000 Mbits/s?
    Bit rate  throughput
  Function of topology, number of devices, and traffic
Controller/instrument capacity
  Network controllers
  Network enabled instruments
    Instruments are often the limiting factor
Physical
Data Link
Network
Transport
Application
Notes: The throughput of your overall network system relies on the network capacity, the controllers, and instrument capacities. When a network is described by Mbits/s, this refers to the amount of time it takes to transmit a bit on the Ethernet channel. It does not mean that your application gets that much throughput. The network capacity is affected by several factors. Since the Ethernet is a shared access network, the fewer the devices in the network, the higher the capacity for data transmission. Also, the traffic those devices add to the network is a key component. Not all devices need to transmit and receive the same amount of data – this adds a new variable to the equation. Because there are unlimited topology configurations possible, every network system is different and could be studied separately.
Note though, for internal or controlled networks, data transfer speed is often not the bottleneck. Often, the limitation lies with the devices themselves. If the devices are networked enabled, it relies on their capacity to transfer that data onto the network. If the devices are not Ethernet-enabled and require a controller to integrate them into the networks (for example GPIB and Serial devices), the capacity of those controllers also affects the overall system throughput.

## Slide 19
Router
Local Traffic
Local Traffic
Bridge
Network Design Factors 3. Throughput
Subnet 1
Subnet 2
Subnet 3
Physical
Data Link
Network
Transport
Application
Hub
Hub
Bridges can be used to reduce traffic
Notes: In a dedicated line, the maximum bit rate of the network (10, 100, or 1,000 Mb/s) is sufficient for many applications. However, because Ethernet is a shared access network, the achievable rate of throughput for a given application depends also on the number of devices communicating on that network and the activity among them. The best way to ensure consistent speed on an Ethernet network is to separate critical network segments using switches or routers. For example, on a 100 Mb/s network, a segment of many devices on the network can be separated by using a switch to give multiple devices their own 10 Mb/s line. This reduces unnecessary traffic from other systems on the network, and enhances the speed at which these devices are networked.

## Slide 20: Network Design Factors 4. Determinism
Ethernet is not deterministic
  Network traffic may cause collisions
  Routers, hubs, and bridges insert delays
  Data integrity = retransmissions
Possible solutions
  Minimize delays
    Limit network traffic
    Limit the number of hubs/bridges/routers
  Minimize traffic
    Use bridges
Physical
Data Link
Network
Transport
Application
Notes: On an Ethernet network, it is not possible to determine when a particular device will actually get to send or receive a message, since all systems on the network can send messages at any time and a device may have to wait for the network to clear before its message is sent. Even though bridges help achieve a more constant data throughput, they insert delays to the overall transmission. To achieve the throughput and determinism that your system requires, you should balance trying to minimize delays and traffic.
While there will always be applications that can not sacrifice determinism, a properly configured networked system can meet the required performance.

## Slide 21: Network Design Factors 4. Determinism
Depends on traffic load
  10%, shared networks
  30%, switched networks
Physical
Data Link
Network
Transport
Application
Router
Local Traffic
Local Traffic
Bridge
Subnet 1
Subnet 2
Subnet 3
Hub
Hub

## Slide 22: Network Design Factors 5. Instrument Sharing
Serial
  One instrument per port (RS-232)
  Up to 31 instruments per network (RS-485)
Computer 1
(a)
(b)
Serial
instruments
Physical
Data Link
Network
Transport
Application
Computer 2
Notes: The ability for different users and stations to share instrument control and monitoring results brings many advantages to networked applications. Different bus specifications require and allow different possible configurations and control styles. If the instruments you need to control are not network-enabled, the controllers that allow you to connect those instruments to the network (plus the bus specification themselves) will determine the possible configurations of the system. For serial instruments, you can control only one RS-232 device per port and up to 31 RS-485 devices per port.

## Slide 23: Network Design Factors 5. Instrument Sharing
GPIB
  14 instruments per controller
Physical
Data Link
Network
Transport
Application
Computer 1
(a)
(b)
Computer 2
GPIB
instruments
Notes: By specification, one GPIB controller can control up to 14 devices in one bus. For example, if you have two computers in your system and each is trying to control a different instrument, both instruments could be connected to the same Ethernet-to-GPIB controller and use the same network parameters within the system. The Ethernet-to-GPIB controller behaves like a GPIB controller, so the instruments could be set up in linear or star configuration.

## Slide 24: Network Design Factors 5. Instrument Sharing
Serial – not possible simultaneously
  Requires opening & closing sessions
GPIB – possible with or without locking option
Computer 1
Computer 2
GPIB
instrument
Physical
Data Link
Network
Transport
Application
Notes: When you want to control the same instrument from different computers, you can use GPIB. If you use the locking option available in software, you can have both applications try to access the same instrument, but prevent one application from interfering with the other application’s process. This is helpful when computer 1 needs the instrument to perform a critical task. The application in computer 1 should be able to prevent computer 2 from asking the instrument to do a completely different operation while the critical operation is in process. By locking the communication with the instrument just before the critical task starts and unlocking it after it is finished, computer 1 and 2 can share the instrument and still have control of critical situations. If this locking mechanism is not used, both applications will run, but there is the risk of interfering with the instrument and changing the desired configuration of another application already accessing the instrument.
On the other hand, a serial instrument can only be accessed by one computer at a time. If computers 1 and 2 want to access the instrument, the application software needs to open a session to the instrument and close it when finished, so that the other computer can have access to it.

## Slide 25: Network Design Factors 6. Security
Dedicated networks
  The most secure
  Isolated – no outside access
Shared networks
  Adds risk
  Non isolated – accessible from outside local network
Outside interference can be prevented
  Firewalls
  Application level locking
  Controller features
Physical
Data Link
Network
Transport
Application

## Slide 26: NI and Ethernet Instrument Control Options
Ethernet instrument controllers
  GPIB
  RS232 and RS485
NI-VISA™
  GPIB, serial, VXI, and VXI-11 Ethernet
PXI/VXI
Notes: Several instrument manufacturers have started creating Ethernet-based instruments that you can connect to a network and access and control from any computer in the network. However, only a minimal number of Ethernet-based instruments are currently on the market. Also, you may already have extensive test and measurement systems consisting of numerous instruments. With National Instruments Ethernet-to-GPIB and Ethernet-to-Serial controllers, you can control your exiting GPIB or Serial equipment located anywhere in the world from your own desk via standard Ethernet connection.
We have recently added support of Ethernet-based instruments to NI-VISA. With PXI and VXI modular systems, you can also control your instrumentation systems over Ethernet.

## Slide 27: GPIB-ENET/100
• Run existing code unmodified
• Web enabled with LabVIEW
and Measurement Studio™
• 10/100 Mbits/s networks
• 800 kbytes/s transfer rates
• Configure and use easily
Notes: With the Ethernet-to-GPIB controller, the GPIB-ENET/100, you can easily access remote equipment via TCP/IP protocols on 10BaseT and 100BaseTX networks. By combining a new architecture, 100BaseTX networking capabilities, and the high-speed HS488 protocol, you can enhance performance by more than 10X as compared to existing GPIB controllers. This performance is comparable to that of GPIB plug-in controllers with the flexibility of Ethernet GPIB control.
The GPIB-ENET/100 is easy to use and configure. Any program previously written for other National Instruments GPIB interfaces runs unmodified. You can configure the GPIB-ENET/100 with Dynamic Host Configuration Protocol (DHCP) or with a simple configuration utility. No dip switches or jumpers are required and the controller offers flexible installation options including rack mounting, DIN rail mounting, wall mounting, and stackable standalone use.

## Slide 28: ENET-232 and ENET-485
• 10/100 Mbits/s networks
• 2 and 4 port options
• Configure and use easily
• Uses standard MS serial interface
• Web enabled with LabVIEW and
Measurement Studio
Notes: The National Instruments ENET-232 and ENET-485 serial device servers connect either high-speed (100 Mb/s) or low-speed (10 Mb/s) Ethernet networks to asynchronous serial ports for communication with serial devices. Serial device servers use standard RS-232, RS-422, or RS-485 communications. The TCP/IP communication protocol, which handles all communication between the serial device server and the host PC, runs on embedded firmware within the serial device server. A configuration utility automatically configures the IP address of the serial device server and exposes all additional serial ports to the operating system for immediate use by any application software package using standard Windows serial I/O functions calls.

## Slide 29: NI-VISA™ and Ethernet Support
NI-VISA control of Ethernet instruments
VXI-11
  Ethernet protocol, not a VXI protocol
  Currently used mostly by Agilent instruments
  Good 488.2 protocol for new Ethernet instruments
Raw TCP-IP sockets
  Similar to LabVIEW and LabWindows™/CVI libraries
  Adds control of no-delay and keep-alive options
Notes: <number>
<footer>
<header>
<date/time>
You can control new Ethernet-based instruments with existing NI-VISA code. Our latest version of NI-VISA supports the control of Ethernet-based instruments, in addition to allowing the control of VXI, GPIB, and serial instruments interchangeably. Thus, the high-level software provides you with tools to develop bus-independent instrument drivers efficiently.
The Ethernet implementation in NI-VISA 2.5 provides client support only, which allows a user to connect to a device at a given IP address. It does not implement servant support such as listening for and accepting connections.
For low-level socket communication, the VISA resource name includes the port number, such as "TCPIP::<hostname>::<port>::SOCKET". If an Ethernet device supports the VXI-11 instrument protocol, which is a recommended communication mechanism, the VISA resource name is "TCPIP::<hostname>::INSTR".
Both VISA Ethernet protocols support Write, Read, AssertTrigger, ReadSTB, and Clear. A VXI-11 device also adds SRQ event capability.
If you are an instrument vendor and you plan to support the Ethernet interface, see National Instruments for information on the VXI-11 protocol. Implementing VXI-11 makes it easier for VISA users to integrate your product into their systems.
In NI-VISA 2.5, Ethernet is supported on only Win32.

## Slide 30: Networked PXI and VXI
Notes: VXI Specification, introduced in 1987, provides users with high performance modular systems in which instruments from many vendors work seamlessly in the same mainframe. Because VXI combines sophisticated instrument environment with a modern computer backplane, VXI instruments have the ability to communicate at very high speeds using the best technology from both GPIB instruments and plug-in DAQ boards.
The PXI Specification, introduced in 1997, is an open industry standard that extends CompactPCI for measurement and automation systems. PXI was designed by adding some of the best features of VXI to PCI technology. More than 50 companies have endorsed the specification and are members of the PXI Systems Alliance. PXI maintains interoperability with CompactPCI. There are instruments available for PXI from many vendors.
Since both VXI and PXI systems are able to have embedded computers or external computers with network connections, you could control all these instruments in a very modular, high performance network system. You can combine VXI, PXI, Serial, and GPIB instruments into one system.

## Slide 31: Case Studies and Demonstration

## Slide 32: Summary
Different networking protocols
  TCP/IP is most common
Use existing infrastructure and knowledge
Connect Ethernet based and existing instrumentation in one system
Many factors determine design of system
  Topology, configuration, determinism, instrument sharing, security and so on
  Deterministic, highly secured applications are not recommended

## Slide 33: Questions?