## Slide 1: Distributing Execution Throughout Your Network
Richard McDonell
Application Engineer
Fri Aug 18
12:00-1:15 p.m., 3:30-4:45 p.m.
Pecan (9B)
Notes: Welcome to NIWeek 2000!
In this presentation, we discuss the benefits of distributing measurement and automation executions throughout your network. We also look at some applications where distributed execution is beneficial. Finally, we see how National Instruments software products, namely TestStand™ and LabVIEW™, allow distribution throughout your network.

## Slide 2: Why Distribute Execution?
Increased performance
  High-channel count measurement with data reduction
  Distribute complex analysis to many processors
Remote access
  Physically separated measurement nodes
  Avoid human involvement in harsh environments
Notes: Distributing different portions of a program's execution through a network can significantly increase the performance of a measurement and automation system. For example, you might distribute the analysis of large amounts of data over several computers or distribute execution to provide redundancy in a mission-critical application. It may also be desirable or even requisite that a measurement be taken at a location physically separated from the computer performing the analysis and presenting the data. Applications executed in harsh or dangerous conditions, or throughout a large area where data must be collected, can use network technologies like Ethernet to easily acquire remote data. While low-level protocols provide the basis for communicating between applications, advanced technologies are available for easy distribution and the execution of a program across a network. National Instruments provides a wide array of measurement technologies that integrate seamlessly with Ethernet networks.

## Slide 3: Networking Technologies
Ethernet
  Ubiquitous, inexpensive, widely supported
  10-BaseT 10 MB/s
  100-BaseT 100 MB/s
  Wireless ENET 1-2 MB/s
  On the horizon - 1Gbit/s Ethernet
Notes: Now, let’s define some of the terms associated with network measurement solutions. First, what is a network? A network is simply a collection of different computers or measurement devices linked together. One of the most common technologies for linking these devices is Ethernet. Many measurement devices have Ethernet ports, so Ethernet technology is not limited to computing hardware.
Ethernet has long been a communication infrastructure for business and information technology applications. Until recently, most viewed it only as an information network. Today, its widespread use in offices and manufacturing floors has earned it the reputation as a viable solution for control and device data transmission.
Ethernet is a high-speed networking interface that operates over a variety of media. The most common variations are 10Base2, or thin wire Ethernet, carries signals through a flexible coaxial cable. 10BaseT, or twisted pair Ethernet, carries the signal through a cable consisting of twisted wires. The “10” in the designation indicates that the interface operates at 10 Mbits/s. A 100BaseT variation is also available with interface operations at speeds up to 100 Mbits/s. We can even begin to see quicker interface times some reaching the speed of 1 GBits/s. One significant benefit of Ethernet is that it can span long distances – from 100 m (twisted pair) to more than 2 km (fiber optic) and message latencies of under 5 ms. For even greater distances and flexibility, the Wireless ENET is another variation that allows for wireless interface operations at speeds of 1 to 2 Mbits/s. If you need to monitor and control a system over a long distance, Ethernet and Wireless ENET are optimal choices.
We often speak of two different types of networks – intranets and the Internet. Intranets are internal, self-contained networks, often called Local Area Networks (LANs), which generally belong to a single organization or company and prevent unauthorized access by outsiders. An Internet is simply a combination of many different contributed Intranets from a wide array of locations.

## Slide 4: The Virtual Instrument
Acquire
Analyze
Present
Notes: In the past, engineers and scientists would take the first measurements using electrical devices, such as analog meters, that are crude by today’s standards. Over time, these devices evolved into sophisticated and complex stand-alone instruments, such as spectrum analyzers and vector network analyzers. While delivering a marked increase in measurement capability and flexibility, these instruments had, and still have, a number of limitations. One limitation of the instrument occurs when the user is unable to modify the set of functions or operations; the data acquisition, analysis, and presentation properties of the instrument are pre-determined by the vendor, and are not subject to alteration. In addition, traditional instruments generally lag computers in processing power and data storage capacity.
The whole concept of virtual instrumentation is to create measurement systems by combining measurement hardware and software components with mainstream computer technologies, such as desktop PCs or workstations. By incorporating industry-standard computers into your system architecture, you effectively capture performance, processing power and data storage in your measurement system. PCs and workstations deliver significant gains over traditional instruments in the realm of data analysis and presentation. Because computers are so versatile, your measurement systems automatically inherit another advantage over traditional instruments. Your system can now evolve and change over time according to your needs. The user can simply modify various software and hardware components instead of buying new, costly stand-alone instruments. The benefits of computer-based measurement systems are apparent. Many measurement systems today only contain a single computer. What would happen if we expand the system to include more than one computer or make the system accessible to an entire network? By doing this, you can capture all of the advantages networks provide for your measurement applications.

## Slide 5: The Distributed Virtual Instrument
Acquire
Anywhere
Analyze
Anywhere
Present
Anywhere
Notes: Because computers are linked together in a network, you can naturally transfer data from one computer to another in a variety of forms. Perhaps you want to take data in one location and then send it to another site. Or, you might want to send multiple copies of the same data to other parts of your enterprise. Still, you may need to log measurements periodically to a remote database. All of these scenarios are possible and even practical applications with network measurement systems.
If a network consists of several computers, can you distribute various tasks you want to perform in your measurement application to several different machines? Of course you can, but probably not all of the computers in your network will be identical. Some may have larger disk drives or more physical memory. Some may have better processors, and others may not have any expansion slots available for measurement hardware. Because you have an variety of different computing machines in a network, you have the power to pick and choose which measurement tasks should be performed on which machines. This allows you to optimize the performance of your system. Why not perform the most intensive tasks, on the machines with the best processors and leave less critical tasks to slower computers? You can also preserve the computer infrastructure within your network by distributing execution. If your measurement system requires a substantial amount of processing power, you can just divide your measurement system among several machines instead of purchasing new computer equipment.
Networks are changing the face of measurements by unleashing the potential of your measurement system. With network technologies, you can acquire anywhere, analyze anywhere, and present anywhere…literally.

## Slide 6: Distributed Execution
Acquire
Analyze
Present
Notes: With distributed execution, you execute various tasks in your measurement system across several different computers. Now no one machine becomes stressed under a heavy load of required operations and measurement operations can coordinated across many computers into a single system. Acquire and reduce data at the computer taking the measurement and reduce before data before sending to reduce network congestion.
You can also use distributed execution to control a system remotely by splitting the execution into two parts. In the first part so that the measurement system resides on a remote machine and in the second part the controlling portion resides on a computer in a more comfortable location.
Distributing execution provides some definite advantages. You can selectively choose which portions of your cumulative measurement tasks run on which machines, often in parallel resulting in improved system performance. Also, because you can distribute your application in such a way, no single computer is a bottleneck in your measurement system. These systems will not be taxed. Distributing execution means you can protect your computer capital investment.
A typical measurement solution consists of an acquisition element, an analysis component, and some type of presentation capability. With distributed execution, you can break up these tasks and run each on different computers. Again, no longer is it acquire, analyze, and present – it’s acquire anywhere, analyze anywhere, and present anywhere.

## Slide 7: Distributed Execution Example
Application – wind tunnel for testing jet turbines
Large channel count acquisition
Requires analysis and logging of large amounts of data
Solution – multiple PXI chassis connected by Ethernet
Create client application to acquire and analyze data
Create application on server machine to start client apps and present results
Notes: Let’s look at an example of how distributing execution can improve the performance of a system. Testing complex avionics components, such as jet engines, requires a very large amount of high-speed data acquisition and complex analysis. To sustain throughput requirements of such a high-channel-count system, you can acquire and reduce the data on many computers in parallel. Several PXI chassis with instrument modules can be used to collect the data, reduce it through averaging, and scale the measurements. A single machine can remotely execute the programs on each PXI chassis, compare the reduced data to known good values, display the results, and log data to a database.

## Slide 8: Technologies for Distributed Execution
Remote procedure call (RPC)
  Protocol for calling functions remotely
DCOM/CORBA
  Object-oriented technologies for distributing components over a LAN
SOAP/Jini
  Simpler interfaces for distributing components over the Internet
TestStand™ remote sequence call
LabVIEW™ remote VI call
Notes: You can use several technologies for distributed execution. These include the proven remote procedure call (RPC) based DCOM/CORBA technologies as well as the new protocols that are emerging such as SOAP and JINI.
Currently, DCOM/CORBA are the most widely used technologies for integrating distributed execution functionality in software programs. However, with the introduction of the new SOAP and JINI protocols, distributed execution could increase flexibility with easier implementation.
National Instruments TestStand and LabVIEW software products leverage off of the DCOM technology to make it easy to include distributed execution in your measurement and automation applications. TestStand includes a Remote Sequence Call step to call test sequences across the network. LabVIEW allows for calling VIs on other networked computers using the Remote VI Call.

## Slide 9: DCOM
Distributed Component Object Model
Microsoft technology released in 1996
Allows client and server computers to communicate across the network
Commonly used for performing distributed execution
Notes: DCOM is an abbreviation for Microsoft’s distributed component-based architecture known as distributed component object model. DCOM technology was officially released with Microsoft Windows NT 4 in 1996. DCOM versions for Microsoft’s other Windows operating systems have been released since then. DCOM essentially replaced the previous remote automation technology supported by COM. The DCOM technology is built on the remote procedure call (RPC) protocol to provide a highly efficient and flexible way to perform distributed execution.

## Slide 10: SOAP
Simple Object Access Protocol
Introduced in 1999 by DevelopMentor and Microsoft
Power of RPC and flexibility of XML
Easier to integrate distributed executions
Allows for use on any computer platform
Notes: Simple object access protocol (SOAP) was introduced to the distributed computing community about 18 months ago. SOAP was created by developers and researchers at DevelopMentor and Microsoft in an effort to make it easier to deploy distributed computing through firewalls and across the Internet. When finalized the SOAP protocol should help provide the power of RPC with the flexibility of XML. Because SOAP uses Internet standards such as HTTP and XML, it allows you to employ SOAP to execute RPCs between any combination of otherwise incompatible platforms. It has been suggested that perhaps DCOM could even be implemented on top of SOAP.

## Slide 11: Jini
Announced by Sun Microsystems in 1999
Created for networking all sorts of electronic devices
Idea is to create a plug-and-play type capability for networking equipment
Based on Java for flexibility among platforms
Notes: Sun Microsystems Corporation created the Jini concept. Jini created networking for electronic devices. Not only does Jini allow for networking devices, but also geared to join them up easily in a plug-and-play manner. This will allow for instantly creating networks of miscellaneous equipment. Jini is based heavily upon the common Java language in an effort to provide the new connection technology with the ability to use different types of computers and microprocessor-based equipment. Also, there are suggestions that Jini is not limited to the domain of network devices and could possibly expand into the wireless world. Nonetheless, the new Jini technology may soon be providing an excellent way to create distributed executions.

## Slide 12: TestStand Remote Sequence Call
Uses DCOM technology
Built-in ability to launch subsequences anywhere over the LAN
Can pass parameters to/from remote sequences
Notes: Typically, distributed systems are complex and daunting to write, because they require a great amount of programming to pass data between two computers or to execute calls on remote machines. Often you must fully understand complex programming concepts like remote procedure calls (RPC) or remote method invocation (RMI). Fortunately, there are tools that take the complexity out of distributing system execution.
TestStand™, a test executive and test management environment, has a remote sequence call. This feature greatly simplifies the creation of distributed production test systems by masking much of the complicated code from the user.

## Slide 13: Remote Sequence Call Example
TestStand sequence
Init
Generate
report
Unit under test
Seq A
Seq C
Seq B
Notes: Example
TestStand can sequence tests written in LabVIEW, Measurement Studio, LabWindows/CVI, Visual Basic, Visual C++, and other test languages. It delivers intelligent sequencing (branching, looping, etc.), report-generation, and database connectivity.
TestStand’s distributed architecture allows you to run tests painlessly on remote machines. Using this client-server model, a single computer can sequence through a series of tests and archive the results. Each test is run on a different networked machine. A distributed architecture allows you to decrease test time, and improve efficiency of your production line by creating tests that pass information to each other over a network. This process is often called parallel testing and can greatly improve your production test throughput.

## Slide 14: Remote Sequence Call Demo
Client
Server
Sweep 0
Sweep 1
Sweep 2
Sweep 3
Sweep 4
Sweep 5
Sweep 6
Sweep 7
Distributed execution
Notes: Demonstration
To demonstrate the use of the remote sequence voltage call in TestStand, we created an example that allows the user to execute four voltage and power sweeps on the client computer, and distribute the other four sweeps to the server computer for a total of eight sweeps. This example illustrates how to distribute the executions to another computer as well as the time saved when testing multiple UUTs at once. First, we will run the test sequence so that four sweeps run on the client computer only. Second, we will run the test sequence so that four additional sweeps run on the remote computer using a remote sequence call. This example can also be found in our example programs database located at ni.com/support/epd

## Slide 15: Remote Execution Options
Remote execution
Specify host by expression
Remote host
Notes: In TestStand, you can enable the remote server to accept remote execution requests from a client machine by enabling the Enable Remote Execution option on the Remote Execution tab of the Station Options dialog box.
Options available on the Remote Execution tab are listed below with a description of each:
Remote Execution – selects whether TestStand executes the sequence call on a remote host.
Specify host by expression – selects whether you specify the remote host name through literal strings or through expressions that TestStand evaluates at run-time. When disabled, you can use the Browse button to select a remote host name on the network. When enabled, you can use the Browse button to build an expression.
Remote Host – contains the name of the remote host.

## Slide 16: Rengine
Rengine allows TestStand to act as a server
Initiate server by running Rengine.exe
Notes: TestStand utilizes the DCOM features in Windows-based platforms to perform the distributed execution of a test sequence. When using TestStand to execute a test sequence on a remote machine, you need to configure the DCOM settings on your client and server computers. In general, before you can communicate with a server via DCOM, you must configure the security permissions for the server on the Windows system of the server. The Windows system security permissions can be configured using the DCOMCNFG utility.
If you want TestStand to invoke a sequence on a remote TestStand server host, properly configure the server on the remote system. You must enable the TestStand server to accept remote execution requests, the server must be registered with the operating system, and you must configure the Windows system security of DCOM to allow users to access and launch the server remotely.
A TestStand server is active when the TestStand application, TestStand\bin\Rengine.exe, is running on the remote system. Each TestStand client communicates with a dedicated version of the remote engine application. In Windows NT, the remote server launches automatically. Each time a TestStand client uses the server. In Windows 95 and 98, you must launch the remote server manually, and only one client is able to use the server at a time. You can automatically launch the server by placing a shortcut to the application in the startup folder on the server system.

## Slide 17: LabVIEW Remote VI Call
Allows you to easily distribute the execution of VIs
Distribute as much or as little of your program as you like
Provides easy crossplatform remote connectivity
Notes: LabVIEW has a feature similar to TestStand’s remote sequence call known as the remote VI call. When you use a remote VI call, you simply select the LabVIEW code you wish to execute remotely. For text-based languages, like C or C++, this technique is referred to as a remote procedure call (RPC) or remote method invocation (RMI) in Java. Both of these techniques can be difficult to implement, because they require specific knowledge of the network environment, along with several programming steps. Many consider RPC an expert programming topic.
Combining the remote VI call with LabVIEW’s hierarchical nature, you can distribute as little or as much of your program as you wish. Not only can you distribute the data acquisition, but also the analysis, decision logic, or any part of your program that can be encapsulated in a LabVIEW VI. A LabVIEW VI is parallel to a subroutine, or function, in other programming languages. Using remote VI calls, you can easily execute any VI on any computer.
With a remote VI call, you can even execute a VI on different a platform than the one on which the calling application runs. For instance, you may have an operation designed for a special configuration on a Linux machine that you would like to call from your main program running on Windows 2000. If you use the remote VI call, it makes no difference what processor and operating system are resident on the local and remote machines as long as LabVIEW exists on both.

## Slide 18: Remote VI Call Example
Ethernet Hub
PXI Chassis
Notes: Example
A laptop may not have image acquisition or high speed data acquisition capability. Therefore, we could use the remote VI call on the laptop to perform the image and waveform acquisition on the PXI system, through the workstation, and then analyze and present the data on the laptop.

## Slide 19: VI Server
Conveniently allows for remote VI calls
Can accomplish wide variety of tasks
Commonly used VIs
Notes: You access VI server functions through references to two main classes of objects: the application object and the VI object. Once you create a reference to one of these objects, you pass it to a function that operates on the object. When you are finished with it, close the reference. This programming convention is similar to File I/O and TCP/IP network references.
An important aspect of both application and VI references is their network transparency. This means you can open references to objects on remote machines in the same way you open references to those objects on your own machine. After you open a reference to a remote object, you can treat it exactly the same as a local object, only with a few restrictions. For operations on a remote object, the VI Server takes care of sending the information about the operation across the network and sending the results back. Your program looks virtually identical regardless of whether the operation is remote or local.

## Slide 20: Creating References
Application reference
VI reference
Notes: Open Application Reference
Opens an application reference to another LabVIEW application. If the machine name is left unwired or is an empty string, a reference to the current application is returned. Otherwise, the machine name is treated as a TCP/IP address, and can either be in dotted decimal or domain name notation.
Open VI Reference
Opens a reference to the specified VI in the specified application. VI path can be relative to the calling VI’s directory. When a string is wired to this input, it must contain only the VI name and the VI must already be in memory.
Keep in mind that when you have a reference to a VI, you load it into memory. Once you have the reference, the VI stays in memory until you close the reference. It is possible that multiple references to a VI might open at the same time.
In that case, the VI stays in memory until all references to the VI are closed. With a reference to a VI, you can obtain all the properties of the VI, as well as dynamic properties, such as front panel window position. You can also programmatically print the VI, save it to another location, and export or import its strings for translation purposes.

## Slide 21: Using References
Polymorphic with respect to reference input
Notes: Many of the available operations on Application and VI references are only available through the Property and Invoke nodes. Each node has two inputs and two outputs at the top, and a variable list of inputs and outputs below that. Both nodes are polymorphic with respect to the reference input. When you wire an Application or VI refnum to this input, the node automatically adapts to that data type, and makes applicable operations available. With the Property node you can get (read) and set (write) various properties on an application or VI.
You can select the properties from the node pop-up menu by simply clicking a property terminal with the Operating tool, or pop up on the terminal. With the Invoke Node you can perform actions, or methods, on an application or a VI. Unlike the Property node, a single Invoke node executes only a single method on an application or VI. You access the available methods by clicking the method terminal with the Operating tool, or popping up on the terminal, which is the same as the Property Node.

## Slide 22: Remote VI Call Demo
Client
Server
Set control values
Run client VI
Display data from server
Stop client and server
Started by client
Read client controls
Acquire data
Send data to client
Notes: Demonstration
To demonstrate the use of the remote VI call in LabVIEW, we have developed a very simple VI that reads temperature values and plots them on a chart until the stop button is pressed. First, we will run the entire application on the client computer by specifying a local VI as the server. Second, we will split a portion of the LabVIEW code, run the data acquisition portion on a remote computer, but still control the entire process through the client computer.

## Slide 23: Questions?
Notes: ni.com
Please do not hesitate to contact us if you have any questions about building computer-based measurement and automation applications.